## Slide 1: Cell Density-driven Detailed Placement with Displacement Constraint
Wing-Kai Chow, Jian Kuang, Xu He, Wenzan Cai, Evangeline F.Y. Young
The Chinese University of Hong Kong
{wkchow, jkuang, xhe wzcai, fyyoung}@cse.cuhk.edu.hk
ISPD 2014, Petaluma, CA

## Slide 2: Outline
Motivation
Problem formulation
Global Move
Local Move
Experimental Results

## Slide 3: Motivation
Global placement optimizes the target objective
Legalization removes cell overlap and aligns the cells to placement sites with preservation of GP quality
Detailed placement further optimizes the target objective with preservation of GP and legalization quality

## Slide 4: Motivation
Modern placement is usually an optimization problem with multiple objectives
The previous works on detailed placement do not consider the impact of cell movement to the global placement solution
Detailed placer should either
  Target at the same set of objectives, or
  Minimize the perturbation to the solution.

## Slide 5: Problem Formulation
Based on the ICCAD-2013 detailed placement contest
Given:
  A legalized global placement solution
  A target density
  A displacement constraint,
Our objective:
  To minimize total wire-length
  To minimize target density overflow
With constraints:
  All cells are moved within the displacement constraint

## Slide 6: Problem Formulation
Wire-length:
  Measured in half perimeter wire-length (HPWL)
Maximum displacement:
  The maximum move distance from the original position

## Slide 7: Problem Formulation
Cell density:
  Average Bin Utilization (ABU):
    Average bin density of the top γ% highest bin density, where
  Overflowγ is defined as:
  Scale is defined as weighted sum of overflows under different γ
    Higher weights on peak utilization
  Scaled wire-length is calculate as:

## Slide 8: Problem Formulation
Detailed placement problem:

## Slide 9: Our Proposed Algorithm
Global Move : move cell into a good bin
Local Move : adjust cell position
  Vertical Move : move vertically
  Local Reordering : exchange position with neighborhood
  Compaction : shift cells to further minimize wire-length

## Slide 10: Legalized Cell Move
Disadvantages of legalization afterward:
  Legalization usually increase wire-length
  Cell movement in legalization can harm density
  Legalization can bring a cell further away from its original location, which may violate displacement constraint
We propose an operation of Legalized Cell Move
  A cell move followed by a constrained local legalization
We ensure that every cell move results in a legal solution

## Slide 11: Legalized Cell Move
cell
cell
cell
cell
cell
cell
cell
cell
cell
cell
cell
cell
cell

## Slide 12: Legalized Cell Move
Legalization impact is evaluated as the sum of cell displacement caused on other cells.
Discard the cell move when impact exceeds the limit
cell
cell
cell
cell
cell
cell
cell
cell
cell
cell
cell
cell
cell

## Slide 13: Global Move
The whole placement region is partitioned into regular rectangular bins
Objective in Global Move is to place each cell into the best bin that can minimize sHPWL under the displacement constraint

## Slide 14: Global Move
Optimal Region:
  The region bounded by the median of the x- and y-coordinates of a cell’s associated nets, after removing the cell from the nets.
  The region is expanded when it is too small
optimal region

## Slide 15: Global Move
Max-displacement Region
  The movable range of each cell under the maximum displacement constraint
original location
current location

## Slide 16: Global Move
The bins overlapped with both regions are selected as candidate bins
Several random placement sites in each candidate bin are selected and the cost of cell move is calculated, assuming that all other cells are fixed
The cost of moving cell c into a bin b:
The cell is moved into the selected placement site with the lowest cost
Total sHPWL improvement is calculated after each round of Global Move, and repeats until improvement drops below the threshold
max-displacement region
optimal region

## Slide 17: Local Move
After Global Move, all movable cells are allocated to appropriate bins that can minimize total sHPWL
Local Move adjust the position to further minimize the objective
Three sub-steps:
  Vertical Move
  Local Reordering
  Compaction

## Slide 18: Vertical Move
For each cell, the expecting sHPWLs of moving the cell vertically to several nearby rows are calculated.
The cell is shifted to the target location with the lowest resulting sHPWL.
The impact of Legalized Cell Move on sHPWL can be large since the sHPWL reduction is usually small.
Legalization impact limit is defined dynamically for each cell move as

## Slide 19: Local Reordering
Like many other detailed placement approaches, all permutation of cell order in a window are examined and the order with lowest objective cost is selected
Local reordering examine all permutation of ordering three consecutive cells within the same placement segment
No legalization is required as the result of local reordering is always legal
A
B
C
A
B
C

## Slide 20: Compaction
Cells are moved to their optimal position while maintaining the cell order in a row
The problem is defined as fixed order single segment placement problem and it is optimally solved
We extends the algorithm with consideration of placement density and maximum displacement constraint for each cell
The algorithm is based on the Single-Segment Clustering algorithm of FastPlace-DP
Wire-length is optimal when cells or clusters are placed in their optimal region, or the position closest to the optimal region when the optimal region is not reachable
A
B
C
D
A
B
C
D

## Slide 21: Compaction
Displacement range: the bounds on the x-coordinate of a cell that is within the maximum displacement constraint within the segment
Critical bins: the bins that will have cell density overflow when the whole target segment if sully occupied by cells
rangedisp
rangecbin2
rangecbin4
rangedisp – rangecbin2 – rangecbin4
rangeactual
bin1
bin2
bin3
bin4
bin5
cell or cluster of cells
placement segment

## Slide 22: Compaction
rangedisp
rangecbin2
rangecbin4
rangedisp – rangecbin2 – rangecbin4
rangeactual
bin1
bin2
bin3
bin4
bin5
cell or cluster of cells
placement segment
Actual movable range: the bounds on the x-coordinate of a cell that can move to without violating the displacement constraint and worsening bin density overflow

## Slide 23: Compaction
For each segment
  Move cells to their optimal position within its movable range
  While there is any cell/cluster overlapping
    Merge overlapping cells/clusters into one cluster
    Move cells/clusters to their optimal position within its movable range
  Unmerge the clusters to output cell positions

## Slide 24: Compaction
Example:
  Input placement
  Move cells to optimal positions
  Merge overlapping cells into clusters
  Move clusters to optimal positions
  Merge overlapping clusters
  Move clusters to optimal positions
  Output placement
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
AB
EF
C
D
AB
EF
C
D
ABC
EF
D
ABC
EF
D

## Slide 25: Experimental Results
Comparison with FastPlace-DP
Comparison with contestants in ICCAD-2013 contest

## Slide 26: Experimental Results: HPWL (no constraint)
 | FastPlace-DP |  |  |  | Ours |  |  | 
 | Dmax | Davg | HPWL | ΔHPWL | Dmax | Davg | HPWL | ΔHPWL
superblue1 | 11019 | 164 | 3.007 | -11.32% | 33563 | 115 | 2.971 | -12.37%
superblue5 | 16889 | 176 | 3.580 | -9.46% | 28640 | 140 | 3.556 | -10.09%
superblue7 | 25327 | 169 | 4.216 | -11.86% | 31594 | 113 | 4.220 | -11.79%
superblue10 | 19573 | 161 | 5.648 | -7.52% | 37981 | 115 | 5.609 | -8.16%
superblue11 | 40207 | 151 | 3.586 | -9.05% | 41590 | 112 | 3.546 | -10.07%
superblue12 | 24361 | 211 | 2.866 | -15.84% | 25009 | 100 | 2.881 | -15.40%
superblue16 | 25511 | 138 | 2.746 | -10.21% | 24744 | 112 | 2.736 | -10.53%
superblue19 | 22631 | 129 | 1.501 | -10.20% | 24000 | 100 | 1.487 | -11.04%
 |  |  | 1.006 | -10.68% |  |  | 1.000 | -11.18%

## Slide 27: Experimental Results: HPWL (displacement constraint)
 |  | FastPlace-DP |  |  |  | Ours |  |  | 
 | Ddisp | Dmax | Davg | HPWL | ΔHPWL | Dmax | Davg | HPWL | ΔHPWL
superblue1 | 300 | 1199 | 72 | 3.186 | -6.04% | 300 | 55 | 3.148 | -7.17%
superblue5 | 320 | 902 | 84 | 3.729 | -5.72% | 320 | 69 | 3.677 | -7.02%
superblue7 | 400 | 1165 | 83 | 6.367 | -8.73% | 400 | 68 | 4.342 | -9.24%
superblue10 | 440 | 1417 | 89 | 5.763 | 5.64% | 440 | 69 | 5.714 | -6.44%
superblue11 | 440 | 1072 | 85 | 3.691 | -6.38% | 440 | 66 | 3.638 | -7.73%
superblue12 | 360 | 1335 | 86 | 2.983 | -12.25% | 360 | 66 | 2.980 | -12.51%
superblue16 | 300 | 934 | 77 | 2.828 | -7.55% | 300 | 62 | 2.808 | -8.18%
superblue19 | 300 | 629 | 67 | 1.550 | -7.30% | 300 | 54 | 1.534 | -8.24%
 |  |  |  | 1.067 | -6.04% |  |  | 1.000 | -8.32%

## Slide 28: Experimental Results: HPWL – ICCAD2013 Contest
 | Short (Dmax= [150,220]) |  |  |  | Long (Dmax = [15000,25000]) |  |  | 
 | A | C | D (Ours) | Ours | A | C | D (Ours) | Ours
superblue1 | 3.231 | 3.209 | 3.214 | 3.213 | 3.047 | 3.016 | 3.012 | 3.009
superblue5 | 3.783 | 3.750 | 3.775 | 3.774 | 3.648 | 3.647 | 3.649 | 3.648
superblue7 | 4.482 | 4.428 | 4.441 | 4.437 | 4.313 | 4.298 | 4.294 | 4.289
superblue10 | 5.824 | 5.796 | 5.799 | 5.796 | 5.690 | 5.680 | 5.670 | 5.666
superblue11 | 3.738 | 3.705 | 3.718 | 3.716 | 3.616 | 3.617 | 3.613 | 3.611
superblue12 | 3.098 | 3.064 | 3.063 | 3.061 | 2.974 | 2.972 | 2.964 | 2.961
superblue16 | 2.885 | 2.867 | 2.867 | 2.867 | 2.798 | 2.797 | 2.781 | 2.780
superblue19 | 1.584 | 1.573 | 1.575 | 1.574 | 1.532 | 1.536 | 1.527 | 1.525
 | 1.008 | 1.000 | 1.002 | 1.002 | 1.005 | 1.003 | 1.001 | 1.000

## Slide 29: Experimental Results: scale– ICCAD2013 Contest
 | Short (Dmax= [150,220]) |  |  |  | Long (Dmax = [15000,25000]) |  |  | 
 | A | C | D (Ours) | Ours | A | C | D (Ours) | Ours
superblue1 | 0.000 | 1.000 | 0.030 | 0.020 | 0.060 | 0.490 | 0.010 | 0.010
superblue5 | 2.080 | 3.250 | 0.740 | 0.660 | 0.990 | 2.720 | 0.170 | 0.130
superblue7 | 0.000 | 1.000 | 0.010 | 0.000 | 0.040 | 0.220 | 0.000 | 0.000
superblue10 | 0.010 | 0.260 | 0.010 | 0.000 | 0.100 | 0.150 | 0.000 | 0.000
superblue11 | 0.040 | 1.000 | 0.040 | 0.030 | 0.150 | 0.570 | 0.020 | 0.020
superblue12 | 0.000 | 0.060 | 0.120 | 0.000 | 0.180 | 0.000 | 0.100 | 0.000
superblue16 | 0.000 | 0.000 | 0.000 | 0.000 | 0.030 | 0.000 | 0.000 | 0.000
superblue19 | 0.000 | 0.150 | 0.110 | 0.030 | 0.160 | 0.120 | 0.170 | 0.030
 | 2.878 | 9.081 | 1.432 | 1.000 | 9.000 | 22.474 | 2.474 | 1.000

## Slide 30: Experimental Results: sHPWL– ICCAD2013 Contest
 | Short (Dmax= [150,220]) |  |  |  | Long (Dmax = [15000,25000]) |  |  | 
 | A | C | D (Ours) | Ours | A | C | D (Ours) | Ours
superblue1 | 3.231 | 3.230 | 3.215 | 3.214 | 3.049 | 3.030 | 3.013 | 3.009
superblue5 | 3.862 | 3.871 | 3.803 | 3.799 | 3.684 | 3.747 | 3.655 | 3.652
superblue7 | 4.482 | 4.450 | 4.441 | 4.437 | 4.315 | 4.307 | 4.294 | 4.289
superblue10 | 5.825 | 5.811 | 5.799 | 5.797 | 5.696 | 5.689 | 5.670 | 5.666
superblue11 | 3.740 | 3.751 | 3.720 | 3.717 | 3.621 | 3.638 | 3.614 | 3.611
superblue12 | 3.098 | 3.066 | 3.067 | 3.061 | 2.979 | 2.972 | 2.967 | 2.961
superblue16 | 2.885 | 2.867 | 2.867 | 2.867 | 2.798 | 2.797 | 2.781 | 2.780
superblue19 | 1.584 | 1.576 | 1.577 | 1.574 | 1.535 | 1.538 | 1.529 | 1.526
 | 1.008 | 1.005 | 1.001 | 1.000 | 1.007 | 1.008 | 1.001 | 1.000

## Slide 31: Thank you

## Slide 32: Appendix - Benchmarks

## Slide 33: Appendix – Placement Density
input
After Global Move
Iteration 1
After Global Move
Iteration 6
Final Solution
After Local Move
Iteration 1