## Slide 1: Coupling-Aware Force Driven Placement of TSVs and Shields in 3D-IC Layouts
Caleb Serafy and Ankur Srivastava
Dept. ECE, University of Maryland

## Slide 2: 3D Integration
Vertically stack chips and integrate layers with vertical interconnects
  Through Silicon Vias (TSVs)
Advantages:
  Smaller footprint area
  Shorter global wirelengths
  Heterogeneous Integration
Disadvantages:
  TSV-TSV coupling
  TSV reliability
  Increased power density
  Trapped heat effect

## Slide 3: TSV-TSV Coupling
TSVs have large capacitance to substrate
Substrate is conductive: low noise attenuation
Coupling between TSVs must be minimized in order to maximize switching speed
SOLUTIONS: TSV spacing and TSV shielding

## Slide 4: TSV spacing
Spacing between TSVs can reduce coupling
  But requires large distance
Shield insertion can reduce coupling when spacing is small

## Slide 5: TSV spacing
Spacing between TSVs can reduce coupling
  But requires large distance
Shield insertion can reduce coupling when spacing is small
d=12

## Slide 6: TSV Shielding
Shielding: place a grounded conductor between two wires
  EM waves cannot pass through shield, reducing coupling between wires
  Guard ring is less effective with TSVs
  TSVs require shielding throughout the thickness of the silicon substrate
  use GND TSV as shield
Optimal shield placement requires chip-scale coupling models
Analog Transistor

## Slide 7: Previous Work
Geometric model of coupling
  Circuit model of coupling too complex for chip-scale optimization
  Developed model of S-parameter based on relative TSV positions
  Used curve fitting on HFSS simulation data
Shield insertion algorithm
  Based on fixed signal TSV locations, place shield TSVs to minimize coupling
  Solved using MCF problem formulation
Avenue for improvement
  Shield insertion cannot mitigate coupling if spacing is too small
  Determine signal and shield positions simultaneously
[Serafy et. al GLSVLSI’13]

## Slide 8: Force-Driven Placement (FDP)
Input: Fixed transistor placement
Output: Placement for signal and shield TSVs
Objective: place signal and shield TSVs
  Minimize some cost function
Force: derivative of cost function
Solution: find total force F=0
Iteratively solve for F=0 and then update forces based on new placement

## Slide 9: Forces
  Wirelength (WL) Force: pulls objects towards position with optimal wirelength
  Overlap Force: repels objects from one another when they overlap
  Coupling Force: repels each signal TSV from its most highly coupled neighbor
    Coupling evaluated using our geometric model
  Shielding Force: Pulls shield TSVs towards the signal TSVs it is assigned to

## Slide 10: Proposed Algorithm
Assumption: Transistor cells are already placed, limiting the possible locations of TSVs (whitespace)
Step 0: assign each signal TSV to a whitespace region
Step 1: perform coupling aware placement until equilibrium
Step 2: insert shields using our shield insertion method
Step 3: repeat coupling aware placement until equilibrium

## Slide 11: Proposed Algorithm
Assumption: Transistor cells are already placed, limiting the possible locations of TSVs (whitespace)
Step 0: assign each signal TSV to a whitespace region
Step 1: perform coupling aware placement until equilibrium
Step 2: insert shields using our shield insertion method
Step 3: repeat coupling aware placement until equilibrium
Coupling Force Repels TSVs
Shield Reduces Coupling Force
WL force attracts TSVs back together

## Slide 12: Initial Placement
Each signal TSV must be assigned to a whitespace region
  Once assigned TSVs cannot change regions
Objective:
  Minimize wirelength
  Constrain #TSV assigned to each region

## Slide 13: Simulation Setup
 |  | Coupling Aware Placement | 
 |  | Without | With
Shield Insertion | Without | Traditional | CA
 | With | SI | CA+SI
Four Cases
  Traditional Placement: WL and overlap force only
  Placement with coupling force (CA)
  Placement with shield insertion (SI)
  CA+SI

## Slide 14: Experimental Results
CA+SI required less shields than SI alone
Improvement due to CA+SI is greater than the sum of CA and SI alone
Change in total WL is an order of magnitude smaller than improvement to coupling

## Slide 15: Illustrative Example
Without Shields
With Shields
Coupling Unaware
Coupling Aware
CA+SI
CA
SI
Traditional

## Slide 16: Future Work
We have shown that signal and shield TSV placement must be done simultaneously
Also, coupling aware placement and shield insertion are complementary techniques
This approach should be integrated with transistor placement
  Larger solution space
  No assumptions about TSV and transistor placement
  Optimize area
    Instead of adding a fixed amount of whitespace for TSVs during transistor placement

## Slide 17: Questions?

## Slide 18: Backup Slides

## Slide 19: Simulating Coupling
S-parameter (S): ratio of energy inserted into one TSV to energy emitted by another
  Insertion loss, i.e. coupling ratio
HFSS: Commercial FEM simulator of Maxwell’s equations
  HFSS data is used as golden data to construct model
Our model is for specific physical dimensions. The modeling approach can be reapplied for different dimensions.

## Slide 20: Modeling Approach
In HFSS:
  Model two signal TSVs
    Sweep distance d between them
  Add a shield
    Sweep d and shield distance y
    x value does not change results
  Add a second shield
    Sweep y1 and y2
Fit S(d,y1,y2) to HFSS data using curve fitting

## Slide 21: Modeling Approach
In HFSS:
  Model two signal TSVs
    Sweep distance d between them
  Add a shield
    Sweep d and shield distance y
    x value does not change results
  Add a second shield
    Sweep y1 and y2
Fit S(d,y1,y2) to HFSS data using curve fitting

## Slide 22: Modeling Approach
In HFSS:
  Model two signal TSVs
    Sweep distance d between them
  Add a shield
    Sweep d and shield distance y
    x value does not change results
  Add a second shield
    Sweep (x1,y1) and (x2,y2)
Fit S(d,x1,y1,x2,y2) to HFSS data using curve fitting

## Slide 23: Modeling Approach
In HFSS:
  Model two signal TSVs
    Sweep distance d between them
  Add a shield
    Sweep d and shield distance y
    x value does not change results
  Add a second shield
    Sweep (x1,y1) and (x2,y2)
Fit S(d,x1,y1,x2,y2) to HFSS data using curve fitting

## Slide 24: Modeling Approach
In HFSS:
  Model two signal TSVs
    Sweep distance d between them
  Add a shield
    Sweep d and shield distance y
    x value does not change results
  Add a second shield
    Sweep (x1,y1) and (x2,y2)
Fit S(d,x1,y1,x2,y2) to HFSS data using curve fitting

## Slide 25: Extension and Validation
Double shield model:
  Add results from single shield model: S(d,y1)+S(d,y2)
  Superposition is not an accurate model
  Subtract overlap M(x1,y1,x2,y2)
Extension to n shields:
  Add results from single shield models: S(d,y1)+…+S(d,yn)
  Subtract overlap M(xi,yi,xj,yj) for each pair of shields
  Assumes higher order overlap is negligible
Create random distributions of 3 and 4 shields
Compare HFSS results to model results
Average Error:
  S3: 3.7 % S4: 9.4 %
  S3: 1.6 dB S4: 4.6 dB

## Slide 26: Coupling Model

## Slide 27: Shield Insertion Algorithm
Poor Solution
Good Solution
For each signal TSV pair we identify the region where a shield could improve the coupling of that pair
Assign a shield to each TSV pair using MCF problem formulation
Objective: provide shielding for each TSV pair while using least number of shields
  Take advantage of region overlap
[Serafy et. al GLSVLSI’13]

## Slide 28: MCF Shield Insertion Algorithm
Each pair of signal TSVs defines a region
  A set of positions that are good candidates for shielding that pair
MCF problem: assigns a shield to each TSV pair
Objective: Maximize ratio of shielding added to shielding required (shielding ratio) for each TSV pair while using least number of shields
From Serafy et. al GLSVLSI’13

## Slide 29: MCF Problem Formulation
Region node for each TSV pair
Point node for each whitespace grid point
Point cost proportional to total shielding ratio
True cost of each shield is independent of amount of flow carried
u = capacity
c = cost
Heuristic:
After each iteration scale cost by number of units of flow carried in previous iteration
From Serafy et. al GLSVLSI’13

## Slide 30: Placement Forces
A: all signal TSVs assigned to this shield
FKOZ is the overlap force
  Prevents a TSV from getting within the KOZ area of a transistor or another TSV
FWL is the wirelength force
  Pushes each TSV towards its respective netbox
  TSVs inside the netbox have minimal WL and FWL = 0
FC is a new force which captures the coupling between two TSVs
  Coupling force is proportional to the coupling between two TSVs
  Each TSV has a coupling force from all other TSVs, but only the strongest coupling force is used to determine movement on each iteration
FShielding pushes shield TSVs towards each signal TSV they are assigned to

## Slide 31: Why max(Fc)
Don’t let many loosely coupled TSVs overpower strongly coupled TSV

## Slide 32: Raw Data
 | Traditional | CA | SI | CA+SI
B1 | -25.0 | -25.3 | -25.2 | -26.2
B2 | -25.3 | -25.5 | -26.1 | -26.5
B3 | -25.3 | -25.3 | -26.1 | -26.4
B4 | -25.3 | -25.6 | -25.2 | -26.5
B5 | -25.3 | -25.3 | -26.3 | -26.4
B6 | -25.3 | -26.3 | -26.1 | -26.4
B7 | -25.3 | -25.7 | -25.4 | -26.4
B8 | -25.2 | -25.3 | -26.1 | -26.4
AVG | -25.3 | -25.6 | -25.8 | -26.4

## Slide 33: Improvement (dB)
 | CA | SI | CA+SI
B1 | -0.3 | -0.1 | -1.1
B2 | -0.2 | -0.8 | -1.2
B3 | 0.0 | -0.7 | -1.1
B4 | -0.3 | 0.1 | -1.2
B5 | 0.0 | -0.9 | -1.0
B6 | -0.9 | -0.7 | -1.0
B7 | -0.4 | 0.0 | -1.0
B8 | -0.1 | -0.9 | -1.2
AVG | -0.3 | -0.5 | -1.1