## Slide 1: Current Density Aware Power Switch Placement Algorithm for Power Gating Designs
Speaker: Zong-Wei Syu
Dep. of EE, National Cheng Kung University
Date: 2014/04/01

## Slide 2: Outline
Introduction
Preliminaries
Problem Formulation
Partition Based Placement Algorithm
  Simplify Model
  Partition and Select Power Switches
  Placement of Power Switches
Framework of Our Methodology
Experimental Results
Conclusion

## Slide 3: Outline
Introduction
Preliminaries
Problem Formulation
Partition Based Placement Algorithm
  Simplify Model
  Partition and Select Power Switches
  Placement of Power Switches
Framework of Our Methodology
Experimental Results
Conclusion

## Slide 4: Introduction
Power-saving becomes a hot issue in VLSI designs because mobile devices are more and more popular.
The power gating technique is widely applied in real designs to resolve the problem.
  It divides circuit into low-power domains and always-on domain.
It is based on the concept of MTCOMS
  Chip performance and power consumption are improved if low cells are used in the low power domain.
  Leakage power problem can be resolved if high power switches are used to turn off the power supply in the low power domain.
Notes: Because mobile devices are more and more popular, Power consumption becomes a serious problem in VLSI design. To resolve the problem, power gating technique is widely applied by industry, it is base on the concept of MTCOMS
If low cells are used in the low power domain, chip performance power consumption are improved. However, low would induce serious leakage power. To resolve the problem, it use high power switches to turn off the power in the low power domain.
Because mobile devices are more and more popular, Power consumption becomes a serious problem in VLSI design. To resolve the problem, power gating technique is widely applied by industry, it is base on the concept of MTCOMS
If low 𝑉𝑇 cells are used in the low power domain, chip performance power consumption are improved. However, low 𝑉𝑇 would induce serious leakage power. To resolve the problem, it use high 𝑉𝑇 power switches to turn off the power in the low power domain.

## Slide 5: Outline
Introduction
Preliminaries
Problem Formulation
Partition Based Placement Algorithm
  Simplify Model
  Partition and Select Power Switches
  Placement of Power Switches
Framework of Our Methodology
Experimental Results
Conclusion

## Slide 6: Two kinds of Power Gating Structures
Two kinds of architectures are proposed to implement power gating designs, which include “fine-grain” and “coarse-grain”.
Fine-grain structure
  Circuits in a low-power domain are divided into several clusters.
  One power switch is inserted into each cluster to control the power-on or power-off for the logic cells in the cluster.
  Design complexity increases.
Notes: The power gating structures are divided into fine-grain and coarse-grain.
( There are two types of power gating structures, one is fine-grain, another is coarse-grain ) 跟上面挑一種講
The fine-grain structure divides the circuit into several clusters in low-power domain, each cluster has its own power switch, each power switch is connected to power supply and control power-on and power-off. But design complexity increases a lot. Thus, fine-grain structure is seldom used today.

## Slide 7: Two kinds of Power Gating Structures (Cont’d)
Coarse-grain structure
  It contains two kinds of power networks as follows:
    Global power network: denoted by VDD
    Local power network: denoted by VDD_OFF
  Power switches are connected between VDD and VDD_OFF.
  Circuits in the low power domain are connected to VDD_OFF.
Notes: Another structure is called Coarse-grain structure. This power network of structure is divided into global power network and local power network. The global power network is denoted by VDD and the local power network is denoted by VDD_OFF. Power pads provide voltage to VDD. All power switches are connected between VDD and VDD_OFF, and controlled turn-on or turn-off by control circuit. VDD_OFF provides power to stand cells in a low power domain.

## Slide 8: Bounding Box of a Low-Power Domain
The shape of a low-power domain is usually not rectangular.
We use a minimum bounding box, which is denoted by , to represent the region of a low-power domain.
  Yellow frame : boundary of chip
  Blue square : always-on domain
  Green frame : low power domain region
  Red frame : minimum bounding box encloses the whole low-power domain
Notes: The outline of a low power domain is usually not rectangular.
  See figure (a) for example, the yellow frame is the boundary of chip, and blue squares denote blocks in always-on domain. After those blocks are placed, the shape of low power domain become irregular. Thus, we use a minimum bounding box B which encloses the low-power domain to represent power switch placement region shown as red frame in figure (b).

## Slide 9: Legal Locations for Power Switches
VSS
VDD_OFF
VDD
Power Switch
Power switches have better to be placed at intersections between VDD stripes and VDD_OFF rows.
  Each power switch has three pins, which are VDD, VDD_OFF, and VSS, respectively
Otherwise, it will waste additional wirelength
row
Notes: In order to reduce routing area, power switches have better to be placed at certain locations in a low-power domain. So we defined legal locations as crossed region between a row and a global VDD stripe. Each power switch has three pins, which are VDD, VDD_OFF, and VSS, respectively. See figure (a). If power switch locations are under global power stripes VDD, they can be connected to VDD through via without using additional metal wire, otherwise they will require additional wire length as shown in figure (b).

## Slide 10: Outline
Introduction
Preliminaries
Problem Formulation
Partition Based Placement Algorithm
  Simplify Model
  Partition and Select Power Switches
  Placement of Power Switches
Framework of Our Methodology
Experimental Results
Conclusion

## Slide 11: Problem Formulation
Input
  A layout that cells are placed and powerplanning is completed
  Power switch library L which contains P types of power switches
    = {}, where ai and ri represent the area and the equivalent resistance of si , respectively.
Output
  Select power switches from L with appropriate sizes and place them at legal locations without any overlap.
Objective
  The target is to minimize the total area of inserted power switches under a given IR-drop constraint as follows:
    : tolerable voltage drop value
    : ideal supply voltage value
    : user specified parameter
Notes: Here shows our Problem Formulation
The input section :
The si denotes one type of power switches.
The output section :
The objective section :

## Slide 12: Outline
Introduction
Preliminaries
Problem Formulation
Partition Based Placement Algorithm
  Simplify Model
  Partition and Select Power Switches
  Placement of Power Switches
Framework of Our Methodology
Experimental Results
Conclusion

## Slide 13: Simplified Model for Power Gating Designs
  The equivalent resistance of power switches in a low power domain can be approximated by this model.
VDD
VDD_OFF
…
…
…
Ri
Ri
Ri
Ri
Ri
Propose a simplified model to approximate required power switches in a power gating design as follows:
  All nodes in a power mesh are consider as one signal node due to mass parallel-connection of power wires with low resistances.
  Each power switch is represented by a resistor
    The voltage-current relation of a power switch can be considered as linear based on the small-signal analysis.
Notes: (In the beginning, if equivalent resistance of power switches in a low power domain can be obtain. We can estimate the precise number of power switches and satisfy the IR-drop constraint based on this value. However the power network is complexity, it is not easy to computed this value.
Thus, we propose a simplified model computing the equivalent resistance of power switches for power gating designs.
All nodes in a power mesh are consider as one signal node because of parallel-connection of power wires with low resistances. Here show original power switch structure based on observing Fig.1 in power gating and transform this figure(Fig.2)
The voltage-current relation of a power switch can be considered as linear, then it is replace by a resistor. Thus, this figure transforms to this figure .
So the power switch can be approximated equivalent resistance model.
In order to satisfy the IR-drop constraint, we try to find the equivalent resistance of power switches. But power gating design is more and more complexity, which becomes not easy to analyze the resistance. Therefore we proposed a simple model.
First all power switches are connected between a global power network and a local power network. Because the power switches exist small voltage variation as linear based on the small signal analysis. Then all power switches transform transistor into equivalent resistance 𝑅_𝑖, making analyze the resistance is easily with model.

## Slide 14: Cutting a Region and the Associated Resistance
Cut B into two parts and and allocate the associated equivalent resistance into and which are and .
  The value R0 (or R1) determines how many power switches will be placed into a region.
  Cost function for cutting a region impacts whether sufficient power switches can be placed into each sub-region and reduce the iteration of procedure
Cost function is as follows:
B0
B1
B
    () is load-current in ().
    () is the number of legal locations for power switches in ().
    α is a user-determinate parameter.
Notes: Based on the model in previous slides. If the equivalent resistance of a region B is obtained, we use a partition base method to cut B into two parts and and allocate the associated equivalent resistance into and . But the cutline location affect whether sufficient power switches can be placed. So we need to cost function to determine the cutline. The main idea of our cost function is to make the load-current and number of legal locations of two regions as close as possible.
Here show our cost function
The first term makes power switches ensure each region have legal location for placing power switches.
The second term tries to reduce iterations number of the procedure.
Given a region B and the associated equivalent resistance 𝑅_𝐵, the region B is cut into two parts, which are denoted by 𝑅_0 and 𝑅_1, respectively. Because cut location may lead to bad result or cause insufficient locations for placing power switches. We use equation (6) as the basis for cutting.
First term try to make the ratio of 𝐶_0/𝑁_0 close to 𝐶_1/𝑁_1 , let two sub region have sufficient legal location placed power switch.
Second term minimizes between 𝐶_0 and 𝐶_1 to reduce iterations of process.
會先給定之前找到的一個bounding box "B"和所有power switch的等效電阻值R_B，之後切割bounding box "B"成兩個subregion，分別等效是B0和B1，因為切割位置和最後的結果有很大的關係，可能切割的不平均使的沒有足夠的位子去放至power switch，所以使用(6)當作切割的依據
(6)第一項是為了兩個subregion有足夠的legal location放置power switch，讓|𝐶_0/𝑁_0 −𝐶_1/𝑁_1 |比值可以接近，第二項是為了minimize |𝐶_0 −𝐶_1|來減少遞迴的次數
給定一個最小可以覆蓋整個低功率電源域的矩形B，以及此電源域中使用的總等效電源開關電阻值RB
首先，將一個電源域切割成兩個子電源域，分別為B0和B1
在切割電源域的時候，切割線的位置對於最後結果，會有很大的影響
式子(6)為我們決定切線位置的函數，令變數C0和C1分別代表切割後兩個子電源域B0和B1的乘載電流和漏電流之總和
變數N0和N1分別代表B0和B1子電源域中，可擺放電源開關器的位置個數 α 是可調整的參數
式子(6)中的第一個項目，是為了使得切割後的兩個子電源域單位可放電源開關器位置所乘載電流值越相近越好
但是，如果只根據這個條件去切割，有時候可能因為 C0 和C1 的差異太大，使得兩邊區域的乘載電流值相距太大，讓兩個子電源域大小不平均，導致總體切割次數劇增，增加程式執行時間
式子(6)也增加第二個項目|C0 – C1| ，為了使得兩邊子電源域B0和B1中，所乘載的電流值C0和C1不會相差太大

## Slide 15: Cutting a Region and the Associated Resistance (cont’d)
  After a region is divided into two parts, we have to allocate the equivalent resistance into two sub-region.
  The resistance (and ) of (and ) can be computed by the following equations:
    The resistance () for power switches is inversely proportional to the summation of the current in sub-region ().
Notes: After a region is divided into two parts, we have to allocate the equivalent resistance into two sub-region.
Because the equivalent resistance for power switch is inversely proportional to the summation of the current and leakage in sub-region , then () can be computed by the following equations
With partition result, we can determine equivalent resistance 𝑅0(𝑅_1) in sub-domain 𝐵0(𝐵_1)
Because the equivalent resistance for power switch is inversely proportional to the summation of the current and leakage in sub-region
The following equation: ……….

## Slide 16: Select Power Switches
Step 1: sort types of power switches in L according to in increasing order
  and is the area and equivalent resistance of
Step 2: pick a type of power switch from L in order and insert as possible number of power switches such that the equivalent resistance of all inserted power switches is larger than R0
Step 3: repeat step 2 until insertion of a new type power switch will make the equivalent resistance is smaller than R0.
’
f
Target equivalent resistance
<
’
  Connect power switches with type by parallel.
’
f
’
>
’
’
X
Notes: After the resistance of each region is determined, this slide shows how to select suitable type and number of power switches from library to constitute the resistor.
Before inserting power switches, we choose types of power switches and sort by area times equivalent resistance from small to large. For example explanation select power switches. is allocated equivalent resistance in the sub-region. First, we pick type of power switches from library and insert of power switches. The makes ’ closest to and larger than . Next time pick type of power switches. The ’ and ’ parallel connection resistors is also larger than . But we add a type of power switch that the parallel resistors is smaller than . So the is approximated to ’ and ’ parallel connection .
Placement of Power Switches can be divided into three steps.
We compute the product of resistance and area, and sort product from small to large in L. Then pick up first power switch, and calculate 〖𝑛𝑢𝑚〗_1 = ⌊𝑟_1/𝑅_1 ⌋ if 〖𝑛𝑢𝑚〗_1is greater than one. The equivalent resistance 𝑟_𝑖^′ equals to 𝑟_𝑖/〖𝑛𝑢𝑚〗_𝑖 . To satisfy the equation 𝑟_1^′ ||𝑅_1^′, the remain equivalent resistance to (𝑟_1′𝑅_1)/(𝑟_1^′−𝑅_1 ). Similarly pick up second power switch, and calculate 〖𝑛𝑢𝑚〗_2 = ⌊𝑟_2/𝑅_1′⌋ if 〖𝑛𝑢𝑚〗_2is larger than one. The process repeats until 〖𝑛𝑢𝑚〗_𝑖 < 1.
We wish close to R0. If
接著選擇適當的power switch，先從power switch集合中排序從小到大，依據𝑎_𝑖×𝑟_𝑖，𝑎_𝑖和𝑟_𝑖分別代表power switches的面積和等效電阻值
先挑選一種power switch去等效目標的電阻值，不足的部分再使用下一種power switch 來等效它，一直重覆下去直到最近接R0 為止

## Slide 17: Placement of Power Switches
Selected power switches of a sub-region are placed by the following procedure:
  Sort the legal locations of the sub-region according to their current loads in decreasing order
  Place the selected power switches into the legal locations in serial from large size to small size

## Slide 18: Partition Based Algorithm
Objective:
  Allocate power switches into a low-power domain with the equivalent resistance
Algorithm Recursive_Partition (Rt , D)
// Rt denotes the total equivalent resistance of a low-power domain D.
1.B = Construction_of_Minimum_Bounding_Box (D)
2.RB = Rt
3.Q.enqueue(B)
4.While !Q.empty() Do
5. B = Q.dequeue()
6. (R0, R1) = CuttingPowerDomain(B, RB)
If ( || || ||
|| )
8. PlacePowerSwitch (B, RB ,L)
9. Else
10. Q.equeue(B0)
11. Q.enqeue(B1)
12.End while
Cut line
Queue
Front
Back
Notes: Here show our partition base algorithm. First, it allocates the bounding box B of a low-power domain D, and RB is set as Rt , where Rt denote the total equivalent resistance of power switches in a low power domain.
Objective:
  Allocate power switches into a low-power domain with the equivalent resistance
Then previous slides shows how to divide a low power domain into two sub-regions and allocate Rt into two sub-region. If any sub-region doesn’t satisfy stop condition, the two sub-regions will be pushed into a queue. Next, a sub-region is pop from a queue. Then the cutline divides it into two sub-regions and the we check stop conditions. If they satisfy the stop conditions we will insert power switches. The algorithm will repeat until the queue is empty.
Our Algorithm allocated power switches into a low-power domain.
We initially found the bounding box B, and R_𝐵 is set as R_𝑡. The R_𝑡 denotes the total resistance of power switches. First B is pushed into a queue. In each iteration, a region B is pop from Q and is cut into two sub-regions. This (r_1/R_0 >N_0 ) denotes that there not exists legal locations. This (𝑟_1/𝑅_0 <1) denotes less than one power switch.
This (N_0==0) denotes .

## Slide 19: Partition Based Algorithm
Algorithm Recursive_Partition (Rt , D)
// Rt denotes the total equivalent resistance of a low-power domain D.
1.B = Construction_of_Minimum_Bounding_Box (D)
2.RB = Rt
3.Q.enqueue(B)
4.While !Q.empty() Do
5. B = Q.dequeue()
6. (R0, R1) = CuttingPowerDomain(B, RB)
If ( || || ||
|| )
8. PlacePowerSwitch (B, RB ,L)
9. Else
10. Q.equeue(B0)
11. Q.enqeue(B1)
12.End while
Objective:
  Allocate power switches into a low-power domain with the equivalent resistance
Queue
Front
Back

## Slide 20: Partition Based Algorithm
Algorithm Recursive_Partition (Rt , D)
// Rt denotes the total equivalent resistance of a low-power domain D.
1.B = Construction_of_Minimum_Bounding_Box (D)
2.RB = Rt
3.Q.enqueue(B)
4.While !Q.empty() Do
5. B = Q.dequeue()
6. (R0, R1) = CuttingPowerDomain(B, RB)
If ( || || ||
|| )
8. PlacePowerSwitch (B, RB ,L)
9. Else
10. Q.equeue(B0)
11. Q.enqeue(B1)
12.End while
Cut line
Objective:
  Allocate power switches into a low-power domain with the equivalent resistance
Queue
Front
Back

## Slide 21: Outline
Introduction
Preliminaries
Problem Formulation
Partition Based Placement Algorithm
  Simplify Model
  Partition and Select Power Switches
  Placement of Power Switches
Framework of Our Methodology
Experimental Results
Conclusion

## Slide 22: Framework of Our Methodology
Rmax =
= (Rmax+ Rmin)/2
Estimate the total equivalent resistance in
  Initial
    : tolerable voltage drop value
    : total current of low power domain
Set the upper bound and lower bound of the equivalent resistance
  = the largest resistance of a power switch in the library
  = 0
Satisfy IR-drop constraint ?
No
Yes
End
Rmin =
= (Rmax+ Rmin)/2
|– | <
And satisfy IR-drop constraint
Yes
No
Initialize the Rt , Rmax , Rm/in
Recursive_Partition_Placemant (Rt ,D)
Place power switches into each sub-regions
Notes:   Here show the Framework of Our Methodology to place power switches. To minimize area of power switches and satisfy IR-drop, we require a precise a value of . Thus we propose method to compute . Since can not be obtain, we set initially. equals tolerable voltage drop value by total current of low power domain. At the same time, Set the upper bound and lower bound .
First Initialize R_𝑡, R_𝑚ax, and R_𝑚in. Because R cannot be obtained by squeezing from R_𝑚ax, and R_𝑚in. Let R_𝑚ax set as largest resistance value of power switches in L and R_𝑚in set as zero. After equivalent resistance is determined, power switches are allocated and placed. To verify IR-drop, we use a static IR-drop analyzer that was implemented by us. If IR-drop doesn’t satisfy constraint, the R_𝑡 is adjusted by binary search method. After the IR-drop several results are obtained, the R_𝑡 is more and more accurate. If voltage drop satisfies the constraint, the R_𝑚in is set as R_𝑡, otherwise R_𝑚ax is set as R_𝑡. If the absolute difference between R_𝑡 and R_t^old is larger than a given 𝜏, the program continues; otherwise, it stops.

## Slide 23: Framework of Our Methodology
Recursively partition low-power-domain into several sub-regions, and allocate the equivalent resistance of power switches into each sub-region.
Place power switches into each sub-region according to equivalent resistance.
Rmax =
= (Rmax+ Rmin)/2
Satisfy IR-drop constraint ?
No
Yes
End
Rmin =
= (Rmax+ Rmin)/2
|– | <
And satisfy IR-drop constraint
Yes
No
Initialize the Rt , Rmax , Rm/in
Recursive_Partition_Placemant (Rt ,D)
Place power switches into each sub-regions
Notes: Based on current .
Then, recursively partition low-power-domain into several sub-regions, and allocate the equivalent resistance of power switches .
Next , place power switches into each sub-region according to equivalent resistance.
Based on current 𝑅_𝑡.
Then, recursively partition low-power-domain into several sub-regions, and allocate the equivalent resistance of power switches .
Next , place power switches into each sub-region according to equivalent resistance.

## Slide 24: Framework of Our Methodology
Analyze IR-drop based on the equation G V = I
  G denotes the conductance matrix.
  V denotes the vector of voltages.
  I denotes the vector of current loads.
Rmax =
= (Rmax+ Rmin)/2
Satisfy IR-drop constraint ?
No
Yes
End
Rmin =
= (Rmax+ Rmin)/2
|– | <
And satisfy IR-drop constraint
Yes
No
Initialize the Rt , Rmax , Rm/in
Recursive_Partition_Placemant (Rt ,D)
Place power switches into each sub-regions
Notes: After power switches are insert to the low power domain, we use a IR-drop analyzer to estimate the quality of design.

## Slide 25: Framework of Our Methodology
Use binary search method to adjust .
  Adjust and according to whether IR-drop constraint of current placement is satisfied:
    YES: set as
    NO: set as
  Set new as ( + )/2
Stop when | - | < γ and IR-drop constraint is satisfied,
  is the current equivalent resistance
  is the equivalent resistance in the last iteration
Rmax =
= (Rmax+ Rmin)/2
No
Yes
End
Yes
No
Initialize the Rt , Rmax , Rm/in
Recursive_Partition_Placemant (Rt ,D)
Place power switches into each sub-regions
Satisfy IR-drop constraint ?
Rmin =
= (Rmax+ Rmin)/2
|– | <
And satisfy IR-drop constraint
Notes: Since initial is incorrect, we use binary search method to find precise , the procedure is as follow in each iteration. Adjust and according to whether IR-drop constraint is satisfied.
The procedure will repeat until the absolute difference of in current iteration and previous iteration is small than a user defined γ value and satisfy IR-drop constraint.
Since initial 𝑅𝑡 is incorrect, we use binary search method to find precise 𝑅_𝑡, the procedure is as follow in each iteration. Adjust 𝑅𝑚𝑎𝑥 and 𝑅𝑚𝑖𝑛 according to whether IR-drop constraint is satisfied.
The procedure will repeat until the absolute difference of 𝑅_𝑡 in current iteration and previous iteration is small than a user defined γ value and satisfy IR-drop constraint.

## Slide 26: Modification of Allocation of Equivalent Resistance
In addition to current distribution, IR-drop in a region is also affected by the following factors:
  distribution of power pads
  density of a power mesh
Adjust the power switch allocation in a region according to the IR-drop value in the previous iterations
  During partition a region into and , the equivalent resistance () in () are adjusted by the following equations:
  () denotes the average voltage drop value in ()
  is a user specified parameter
Notes:   In the partition base algorithm, we allocate power switches into sub-region according to the current in the sub-region. However, IR-drop is affected not only by current distribution but also by distribution of power pads and density of a power mesh.
  To resolve this problem, we further adjust equivalent resistance of a sub-region according to the previous IR-drop value. The equation to adjust equivalent resistance is shown as follows. It will give it small equivalent resistance if the sub-region has a serious IR-drop value in the previous iterations.
However, IR-drop of a region is affected distribution of power pads and density of a power mesh. In order to resolve the above problem, let D_0 (𝐷_1) denote the average voltage drop value, where 𝜏 is a user parameter. Because 𝐷_1/𝐷_0 is close to one, 𝜏 is set small value. To satisfy 𝑅_𝐵=𝑅_0//𝑅_1, we can obtain by 𝑅_1=(𝑅_0 𝑅_𝐵)/(𝑅_0−𝑅_𝐵 ).

## Slide 27: Outline
Introduction
Preliminaries
Problem Formulation
Partition Based Placement Algorithm
  Simplify Model
  Partition and Select Power Switches
  Placement of Power Switches
Framework of Our Methodology
Experimental Results
Conclusion

## Slide 28: Experimental Results
Our algorithm is implemented by C++ programming language and compiled under g++4.6.2.
Our program is run under quad core CPU Intel(R) Xeon(R) E5520 2.27GHz and Cent OS 5.1 workstation with 62GB memory.
The power switches provided by GLOBAL FOUNDRIES 55nm physical libraries.
Notes: TABLE 1 displays the information of the circuits and includes number of stand cells, total power, global VDD, and IR-drop constraint
TABLE 2 shows the information of the power switch and the height, width, and area of each power switch
However, IR-drop of a region is affected distribution of power pads and density of a power mesh. In order to resolve the above problem, let D_0 (𝐷_1) denote the average voltage drop value, where 𝜏 is a user parameter. Because 𝐷_1/𝐷_0 is close to one, 𝜏 is set small value. To satisfy 𝑅_𝐵=𝑅_0//𝑅_1, we can obtain by 𝑅_1=(𝑅_0 𝑅_𝐵)/(𝑅_0−𝑅_𝐵 ).

## Slide 29: Experimental Results
Compare our algorithm with the uniform placement approach and Yong and Ung's algorithm.
  Uniform placement approach
    Evenly insert power switches at legal locations inside a placement region
  Yong and Ung's algorithm
    Define the effect region of a power switch, and place power switches into all legal regions
    Then remove those power switches if their effect regions are overlapped with others.
Notes: The experimental results compare with the uniform placement approach and Yong and Ung's algorithm
  Uniform placement approach is to evenly insert power switches at legal locations
  Yong and Ung's algorithm defines the effect region of a power switch, and place power switches into all legal regions. If effect regions of power switches are overlapped, then remove those power switches.
  The table show that our algorithm has better area and IR-drop than Uniform placement approach and Yong and Ung's algorithm.

## Slide 30: Experimental Results
Placements of power switches and the associated IR-drop maps on Cir.2
Uniform placement approach
Yong and Ung's algorithm
Our algorithm
Notes: Here shows the distribution of power switches in real layout from IC compiler. The yellow point is the location of power switch. The following figures show the associate IR-drop maps. It shows we can use less power switches and satisfy the IR-drop constraint.

## Slide 31: Outline
Introduction
Preliminaries
Problem Formulation
Partition Based Placement Algorithm
  Simplify Model
  Partition and Select Power Switches
  Placement of Power Switches
Framework of Our Methodology
Experimental Results
Conclusion

## Slide 32: Conclusion
Propose an efficient and effective methodology to allocate power switches in power gating designs
  Propose a simple mode to approximate the equivalent resistance of power switches in a region
  Use the binary search method to find proper equivalent resistance in a low power domain
  Use recursively partition based method to allocate power switches
Demonstrate our method can insert less number of power switches and satisfy IR drop constraint comparing to other approaches in experimental results

## Slide 33: End
Thank You For Your Attention