## Slide 1: A Highly-Efficient Row-Structure Stencil Planning Approach for E-Beam Lithography with Overlapped Characters
Jian KUANG, Evangeline F. Y. Young
Department of Computer Science and Engineering
The Chinese University of Hong Kong
香 港 中 文 大 學

## Slide 2: Outline
Introduction
Overall Flow
Sub-problems
Experimental Results
Conclusions

## Slide 3: Outline
Introduction
Overall Flow
Sub-problems
Experimental Results
Conclusions

## Slide 4: Next Generation Lithography
To replace optical lithography and multiple
patterning lithography
  mask cost is too high
Extreme Ultra-Violet (EUV)
Electron-Beam Lithography (E-Beam)
  both are not ready for mass production yet
EUV is delayed by technological difficulties
  such as mask blank defects
E-Beam suffers from low throughput
  bottleneck

## Slide 5: E-Beam Lithography (EBL)
Maskless lithography technology
  shoot a beam of electrons onto a wafer
  and directly creates desired shapes there
  high resolution
  relatively lower cost, compared with the cost of masks
Writing time ~ number of shots
  reducing shot number can improve throughput

## Slide 6: Character Projection
Variable Shaped Beam (VSB)
  every shot can only create one rectangle
  too slow for high-volume manufacturing
Character Projection (CP)
  various characters will be pre-designed
  characters can be placed on the stencil
  a character on the stencil needs only one shot
4 shots are saved

## Slide 7: Stencil Planning
stencil
Figure source: Makoto Sugihara, Optimal Character-Size Exploration for Increasing Throughput of MCC Lithographic Systems. SPIE, 2009
A set of characters are given
Stencil can only take a limited number of characters
Problem: select characters
and put them on the stencil,
to improve throughput

## Slide 8: Row-Structure Stencil with Overlapped Characters
A character has some blank areas surrounding it
  characters can be overlapped to share blank areas
  space can be saved on the stencil
When CP is applied to standard cell design
  all characters have the same size and uniform top
  and bottom blank areas
  only horizontal overlapping need to be considered
  row-structure

## Slide 9: Multi-Column Cell (MCC) System
Layout is divided into regions
Writing time of layout=maximum writing time of each region
  throughput is improved greatly
Regions share the same
stencil design
  to reduce the complexity
We still have one stencil to design, but effects on different regions need to be considered simultaneously
Figure source: B. Yu, et. al. E-blow: e-beam lithography overlapping aware stencil planning for mcc system. In Proc. DAC, 2013.

## Slide 10: Previous Works
Work by Yuan et. al. [1]
  the first systematic study
  greedy and heuristic methods
  slow, no global view
Work by Yu et. al. [2]
  Linear Programming + successive relaxation
  optimality loss because of rounding
  failed to differentiate conventional EBL and MCC system
Work by Chu et. al. [3]
  Stencil planning for flexible character design
[1] K. Yuan, et. al. E-beam lithography stencil planning and optimization with overlapped characters. TCAD, 31(2):167–179, Feb 2012.
[2] B. Yu, et. al. E-blow: e-beam lithography overlapping aware stencil planning for mcc system. In Proc. DAC, 2013.
[3] C. Chu, et. al. Flexible Packed Stencil Design with Multiple Shaping Apertures for E-Beam Lithography. In Proc. ASPDAC, 2014.

## Slide 11: Notations
Characters
has width , blank space and , appears times, and requires shots by VSB
Original shot number
Gain of a character
Shot number
For MCC system
  each region has
  shot number of the layout is

## Slide 12: Problem Formulation
Given a set C of characters, and a stencil of k rows and width W, select a subset of C and decide their positions in the rows of the stencil, such that the width of the stencil is not exceeded. The objective is to minimize the total shot number for the conventional EBL or for the MCC system.

## Slide 13: Outline
Introduction
Overall Flow
Sub-problems
Experimental Results
Conclusions

## Slide 14: Flow Chart
Do this for each row
Character Selection
Row Distribution
Single Row Ordering
Inter-row Swapping

## Slide 15: Outline
Introduction
Overall Flow
Sub-problems
Experimental Results
Conclusions

## Slide 16: Flow Chart
Do this for each row
Character Selection
Row Distribution
Single Row Ordering
Inter-row Swapping

## Slide 17: Single Row Ordering: The Problem
Put characters into a row, order them to minimize
their total length
Solved by travelling salesman problem in previous work
  NP-Complete, very slow

## Slide 18: Single Row Ordering: Our Method – Step 1
Step 1: Construct a graph G
  each character has two weighted nodes for left and right blanks
  weight of edge is the smaller one of the weights of two nodes

## Slide 19: Single Row Ordering: Matching
Call maximum weighted bipartite matching
  If and are matched, should be on the right of
Remove the edges not in the matching solution
Add edges between and for each
Remove the least-weighted edge in the matching solution
Check the directed path from one degree-1 node to
another degree-1 node
  cell order:

## Slide 20: Single Row Ordering: Failed Example with Matching
It only works when path covers all nodes
It fails for this matching solution:

## Slide 21: Single Row Ordering: Our Method
Step 2: Let weightmin be the minimum weight among
all the nodes in G. Update the weight of every node v as
weight(v)− weightmin
Step 3: Remove those nodes with weight 0 and their
corresponding edges.
Step 4: Update all the edge weights according the new node weights to obtain graph G' .
THEOREM: When all the edges in G' are with equal weight (The Constraint), the maximum weighted matching on G' can always give a character ordering with the optimal overlapping space

## Slide 22: Single Row Ordering: Proof
DS is the set of characters that have corresponding
nodes in both U and V
Case 1: |U| = |V| =|DS|,
optimal overlapping is (|DS|-1).we
Case 2: |U| ≠ |DS| or |V| ≠ |DS| ,
optimal overlapping is min{| U |, | V|} .we

## Slide 23: Flow Chart
Do this for each row
Character Selection
Row Distribution
Single Row Ordering
Inter-row Swapping

## Slide 24: Constraint Satisfaction
THEOREM: When all the edges in G' are with equal weight…
Sort: is before iff > or =∧ >
Typically,
Characters in (at most 3) clusters that are
close to one another in the sorted list will
be placed into a row
Satisfy the constraint: Edges in the graph G' are of equal weight 1
Additional advantage: all the blank areas of the characters are distributed regularly

## Slide 25: Redistribution
Rows are divided into groups
Unbalanced distribution of extra blanks in groups
Combine and utilize extra blanks with different types carefully to increase TotalOverlappingSpace

## Slide 26: Flow Chart
Do this for each row
Character Selection
Row Distribution
Single Row Ordering
Inter-row Swapping

## Slide 27: Swapping
A character in one row may be more useful in another row
Deterministic method instead of random method in previous work

## Slide 28: Flow Chart
Do this for each row
Character Selection
Row Distribution
Single Row Ordering
Inter-row Swapping

## Slide 29: Selection
Estimate character number to be selected by average blank space:,
Repeat the selection and placement process as the estimation is not very accurate
Selection for conventional EBL is simple: select the characters with largest gains

## Slide 30: Selection for Marginal Characters
Select characters with highest total gains (summation of gains in different regions)? NO!
First select P containing characters with absolutely high total gains
α is a parameter
Update gains of marginal characters after select P, then select again

## Slide 31: ILP Selection
minimize
s.t.
  , (a)
  , (b)
  (c)
  = 0 or 1, (d)
  is 1 if is selected, is the region number
Number of variables is )

## Slide 32: Outline
Introduction
Overall Flow
Sub-problems
Experimental Results
Conclusions

## Slide 33: Comparison with TCAD’12 Work
[1] K. Yuan, et. al. E-beam lithography stencil planning and optimization with overlapped characters. TCAD, 31(2):167–179, Feb 2012.
benchmark |  | TCAD′12 [1] |  | ours |  | 
data | r# | c# | s# | c# | s# | reduction(%)
1D-1 | 28 | 926 | 50809 | 940 | 19095 | 62.4
1D-2 | 27 | 854 | 93465 | 864 | 35295 | 62.2
1D-3 | 25 | 749 | 152376 | 757 | 69301 | 54.5
1D-4 | 24 | 687 | 193494 | 703 | 92523 | 52.2
1M-1 | 28 | 926 | 53333 | 938 | 39026 | 26.8
1M-2 | 27 | 854 | 95963 | 864 | 77997 | 18.7
1M-3 | 25 | 749 | 156700 | 758 | 138256 | 11.8
1M-4 | 24 | 687 | 196686 | 698 | 176228 | 10.4
1M-5 | 54 | 3629 | 255208 | 3660 | 204114 | 20
1M-6 | 52 | 3346 | 417456 | 3382 | 357829 | 14.3
1M-7 | 49 | 2986 | 644288 | 3016 | 568339 | 11.8
1M-8 | 47 | 2734 | 809721 | 2760 | 731483 | 9.7
Avg. | - | - | - | - | - | 29.6

## Slide 34: Comparison with DAC’13 Work
[2] B. Yu, et. al. E-blow: e-beam lithography overlapping aware stencil planning for mcc system. In Proc. DAC, 2013.
* ILP selection is activated
 | DAC'13 [2] |  |  | ours |  |  |  | 
data | c# | s# | time(s) | c# | s# | reduction(%) | time(s) | speedup
1D-1 | 934 | 29536 | 3.18 | 940 | 19095 | 35.4 | 0.005 | 636×
1D-2 | 863 | 44544 | 3.31 | 864 | 35295 | 20.8 | 0.005 | 662×
1D-3 | 758 | 78704 | 6.98 | 757 | 69301 | 11.9 | 0.005 | 1396×
1D-4 | 699 | 107460 | 6.26 | 703 | 92523 | 13.9 | 0.005 | 1252×
1M-1 | 938 | 45243 | 4.61 | 938 | 39026 | 13.7 | 0.01 | 461×
1M-2 | 868 | 81636 | 6.79 | 864 | 77997 | 4.5 | 0.01 | 679×
1M-3 | 769 | 140079 | 13.76 | 758 | 138256 | 1.3 | 0.56* | 25×
1M-4 | 707 | 179890 | 12.44 | 698 | 176228 | 2 | 0.36* | 35×
1M-5 | 3650 | 227456 | 38.52 | 3660 | 204114 | 10.3 | 0.03 | 1284×
1M-6 | 3388 | 373324 | 53.45 | 3382 | 357829 | 4.2 | 0.03 | 1782×
1M-7 | 3044 | 570730 | 63.52 | 3016 | 568339 | 0.4 | 0.59* | 108×
1M-8 | 2799 | 734411 | 55.27 | 2760 | 731483 | 0.4 | 0.42* | 132×
Avg. | - | - | - | - | - | 9.9 | - | 704×

## Slide 35: Outline
Introduction
Overall Flow
Sub-problems
Experimental Results
Conclusions

## Slide 36: Conclusions
The problem is divided into four subproblems that are solved efficiently
Both conventional EBL and the MCC system are considered
Experiment results demonstrate our efficiency and effectiveness
Significant improvement of throughput
Remarkable speed-up

## Slide 37: Thanks!
jkuang@cse.cuhk.edu.hk