## Slide 1: From Design to Design Automation
Jason Cong
Chancellor’s Professor, UCLA
Director, Center for Domain-Specific Computing
cong@cs.ucla.edu
http://cadlab.cs.ucla.edu/~cong
Notes: 1

## Slide 2: My Summer Internship at Xerox PARC in 1987

## Slide 3: Three-layer channel routing
Channel Density d
    Max. # of crossings over all columns
Lower Bound
    Two layer: d
    Multi-layer [d/L]
    (L: # of horizontal layers)
Layer Assignment
    HVH
My First EDA Paper – ICCAD’1987

## Slide 4: A Two-Layer Channel Routing Solution
1
2
4
3
4
6
6
2
2
1
2
4
3
4
5
6
2
3
5
t1
t2
t3
t4
t5
t6

## Slide 5: Transformation to 3-Layer Channel Routing Solution
t2k-1 k-th track on layer 1
t2k k-th track on layer 2
2 1 5 6 3 4 4 3 2 5
1 2 3 4 2 6 6 4 2
t1
t2
t5
t6
Horizontal Track Assignment
No horizontal wire violation!
Folded track pair may cause vertical constraint violation
Track permutation – two-processor scheduling problem
Adjacent via removal – shortest path formulation
t3
t4

## Slide 6: My First Month at PARC
I was eager to apply combinatorial optimization techniques to more physical design problems …
But Bryan asked me to learn to use the DATools to do a design
DATools at Xerox PARC was state-of-art
  HDL specification and schematic entry
  Floorplan
  Placement
  Global routing
  Details routing
  DRC and LVS …
All written in objected oriented programming style

## Slide 7: My Second Month – Looking where the tool chain needs most improvement
Highland system (UTMC, 1984)
  Builds a minimum spanning tree for each net.
  Edge cost = f(w_length, ch_density, ft's).
Timberwolf (UCBerkeley, 1985)
  Builds a minimum spanning tree for each net based on wire lengths.
  Does simulated annealing with t=0 to improve choices of net segments.
DATools system (Xerox PARC, 1986)
  Minimizes the total number of feedthroughs.
Mowchenko & Ma (Univ. of Alberta, 1987)
  Applies an extended left edge algorithm to each channel.Placement improvement step: swap adjacent cells.
Standard cell design methodology became popular
SC placer Timberwolf was just released, and very successful
SC glabol routing was lagging behind

## Slide 8: Better SC Global Routing Problem Formulation
Connect every net using the minimum area.
  Step 1. Determine feedthroughs
  (i) to complete connections:
(ii) to reduce total channel density
row 3
row 2
row 1
row 3
row 2
row 1
FT
row 3
row 2
row 1
row 3
row 2
row 1
FT

## Slide 9: More on Problem Formulation
Step 2. Determine net segments -- to reduce total channel density.
  A net segment: a pair of pins of the same net in the same channel.
Solution techniques:
Iterative deletion.
A much simplified connection graph yet guaranteeing optimality

## Slide 10: My Third Month: Implementation --Comparisons with Timberwolf4.2
The algorithm is deterministic --- you need to run it only once to obtain good results.
Timberwolf Placer
DATools
G-router
Timberwolf G-router
Placement
global routing
global routing

## Slide 11: Immediate Rewards from Internship
One publication: Standard Cell Global Routing By Iterative Deletion [Cong-Preas, ICCAD’88]
Excitement to see my algorithm produce a real layout
A big layout by Tektronix plotter

## Slide 12: A Life-Time Lesson
As a researcher in EDA, there is a tremendous benefit to be gained from involving VLSI circuit and system designs
  First-hand experience in formulation of new EDA problems
  Development of practical and impactful solutions
A big impact to my career development

## Slide 13: Three Examples from My Career
BOOLEAN MATCHING FOR LUT-BASED FPGA SYNTHESIS
3D IC PHYSICAL DESIGN
HIGH-LEVEL SYNTHESIS

## Slide 14: Example 1: Boolean Match for FPGA Synthesis with Complex PLBs
FPGAs become popular in early 1990s
Most FPGA synthesis algorithms map circuits into uniform-size LUTs
  Including our early work, e.g. FlowMap
But real FPGAs have complex PLBs
XC4K
G
F
H
x

## Slide 15: Example: Mapping to XC4K CLB
Given a function f(0,1,2,3,4,5) where
  a = 1’ + 3, b = 1 + 3
  f = 0’245b’ + 0’245’b + 0’145b + 012’5’a + 0’2’4’5a + 025b + 0’2’5’a’ + 045a’ + 05’b’
How many XC4K CLBs are needed to implement f(0,1,2,3,4,5) ?

## Slide 16: Example: Mapping to XC4K CLB (Cont’d)
G
F
H
3
1
2
0
5
4
The Boolean matching result

## Slide 17
Characterization based on functional decomposition
  f (X) = H ( F (X1) , G (X2) ),
  f(X) = H ( F (X1) , G (X2) , x ),
  f(X) = H (F(X1,x), G(X2), x ),
  f(X) = H (F(X1,x), G(X2,x), x ).
Conditions
  F and G input sizes  4
Result: matched all “difficult examples” (over 1,700) from Xilinx
  Best known tool produced only about 70% match
XC4K CLB
G
F
H
x
f(X)
Boolean Matching Algorithm for XC4K CLB

## Slide 18: Application to Architecture Evaluation -- for MCNC benchmarks
XC4K CLB can implement
  98% of 6-input functions
  88% of 7-input functions
Experiment: enumerate all K-input functions

## Slide 19: Application to Architecture Evaluation (logic capability v.s. silicon area)
XC4K(0,4,3)
24 Memory cells
( > 4 inputs)
G
H
XC4K(3/4,4,2)
28,36 Memory cells
( > 4 inputs)
G
F
H
3,4
XC4K CLB
40 Memory cells
( > 5 inputs)
G
F
H
H1
XC5K
24-48 Memory cells
( > 4 or 5 inputs)
G
F
3,4,5
S

## Slide 20: Example 2: 3D IC Physical Design
Motivations
  DARPA wanted to demonstrate 3D IC technology
  Intel wanted to understand the benefit of 3D architectures

## Slide 21: Thermal Challenges in 3-D ICs
Studied 3D IC Technologies from MIT Lincoln Lab
Key Challenge of 3-D IC Design:
  Higher power density due to the higher device density
  Inter-layer dielectric layers are poor thermal conductors
High Temperature Effects:
  Longer interconnect delays
  Functional failure
Temperature increases dramatically along the Z direction
Z
T
30oC
100oC
135oC
Si 1
Si 2
Si 3
Si 4
150oC
Notes: One of the biggest challenge for 3-D IC design is the high temperature. It has already been an issue for 2-D chips. When it comes to the 3-D ICs, firstly, the power density in 3-D IC is much higher than the 2-D IC since the device density is higher. Also, the dielectric layer between the device layers are poor thermal conductors. Therefore the thermal problem in 3-D IC is even worse. Look at this figure, we can see that the temperature will increase dramatically along the z direction.
The high temperature will make the interconnect delay longer and even cause functional errors. Therefore, a 3-D IC design tool will have to consider the thermal problem.

## Slide 22: Thermal-Aware 3D Physical Design Flow at UCLA (2002 – 2005)
Netlist (LEFDEF)
Design constraints
Technology
CIF/GDSII
Parasitic
Extraction
Thermal
Simulation
Timing
Analysis
Thermal-Driven
3D Floorplanner
Thermal-Aware
3D Router w/
Thermal Via Planning
Open
Access
Thermal-Driven
3D Placement
Compact
Thermal
model
Layout
Verification
Notes: This is the overall framework of the whole 3D physical design flow.
We collaborated with CFD Research corporation on this project. They are responsible for the thermal profiling part and we mainly focus on the tool development.
The inputs include netlist, design constraints, such as timing and temperature constraints, and target 3D technology.
The design flow will go through floorplanning, placement and routing.
The system will output either CIF or GDSII and we will rely on external tools for design verification.
In this talk, I will cover the thermal-driven 3D routing with via planning in detail and will also briefly talk about the floorplanning algorithm.

## Slide 23
10/8/2007
UCLA VLSICAD LAB
23
Tech. Lib
Ref. Lib
Design
3D OA
Thermal-Driven 3D Floorplanner
Thermal-Driven 3D Placer
3D Global Router
Thermal-Via Planner
Tier Export
Tier Import
Detailed Routing by Cadence Router
2D OA
3D Physical Design Flow (IBM, UCLA, and PSU)
(2006 – 2008)
Layer & Design Rules (LEF)‏
Cell & Via* definitions (LEF)‏
Netlist (HDL or DEF)‏
3D RC extraction
Timing
Interface
3D DRC & 3D LVS
Layout (GDSII‏)
EinsTimer
PSU
UCLA

## Slide 24: 3D Physical Design Evaluation (1/3)
Design driver: single-core LEON3
  Synthesized with NCSU standard cell library for MITLL 180nm silicon on insulator (SOI) 3D Integration technology
Statistics of the synthesized LEON3
  #cell = 95061
    Area = 11.05 mm2
  #net = 97880
  #I/O = 150

## Slide 25: 3D Physical Design Evaluation (2/3)
Chip area (utilization = 80%)
  2D implementation: 3.72 x 3.72 mm2
  3-tier 3D implementation: 2.15 x 2.15 mm2
Comparisons
 |  | HPWL (mm) | routed WL (mm) | #TSV | utilization
2D |  | 11.23 | 17.11 | N/A | 0.80
3D | Bottom tier | 2.26 | 3.33 | 0 | 0.80
 | Middle tier | 3.57 | 4.5 | 729 | 0.81
 | Top tier | 2.2 | 2.96 | 1191 | 0.81
 | Total | 8.03 | 10.79 | 1920 | 0.81

## Slide 26: 3D Physical Design Evaluation (3/3)
Bottom tier
Middle tier
Top tier
cells (red)
& TSVs (blue)
Routing congestions

## Slide 27: Flat 3D Placement
UCLA VLSICAD LAB
27
Other
Core
Register file
Cache memory
TLB memory
Debug support
HPWL = 0.99 (m)
#TSV = 3835
Placement (bottom layer, top layer)

## Slide 28: Processor Core Restricted
HPWL = 1.09 (m)
#TSV = 1715
Placement (bottom, top)
UCLA VLSICAD LAB
28
Other
Core
Register file
Cache memory
TLB memory
Debug support

## Slide 29: Register File Restricted
HPWL = 1.20 (m)
#TSV = 845
Placement (bottom, top)
UCLA VLSICAD LAB
29
Other
Core
Register file
Cache memory
TLB memory
Debug support

## Slide 30: Temperature Map
Before Thermal Via Insertion
After Thermal Via Insertion

## Slide 31: Example 3: High-Level Synthesis
In early 2000’s, Synopsys was abandoning their Behavior Compiler
We started research on high-level synthesis
  SOC design was prevailing – embedded processors + customized logic
  E.g. Xilinx Virtex-Pro (with embedded PowerPC core) and Altera Stratix (with Nios)

## Slide 32: xPilot: Behavioral-to-RTL Synthesis Flow [SOCC’2006]
Behavioral spec. in C/C++/SystemC
RTL + constraints
SSDM
Arch-generation & RTL/constraints generation
  Verilog/VHDL/SystemC
  FPGAs: Altera, Xilinx
  ASICs: Magma, Synopsys, …
Code transformation & optimization
  Loop unrolling/shifting/pipelining
  Strength reduction / Tree height reduction
  Bitwidth analysis
  Memory analysis …
FPGAs/ASICs
Frontend compiler (LLVM)
Platform description
Behavior synthesis & optimizations
  Scheduling
  Resource binding, e.g., functional unit binding register/port binding

## Slide 33: xPilot was Licensed to AutoESL for Commercialization
C/C++/SystemC
Timing/Power/Layout Constraints
RTL HDLs & RTL SystemC
Platform Characterization Library
ASICs/FPGAs Implementation
FPGA Prototype
=
Simulation, Verification, and Prototyping
Compilation & Elaboration
Advanced Code
Transformation
Behavioral & Communication
Synthesis and Optimizations
AutoPilotTM
Common Testbench
User Constraints
ESL Synthesis
Design Specification
Platform-based & communication-centric ESL synthesis
Automated ESL-to-GDSII silicon compilation
Rapid platform-based system-level exploration
More than 10X design productivity gain
Notes: AutoPilot provides a novel platform-based, communication-centric ESL synthesis flow that automatically generates high-quality RTL code from behavior-level and system-level C/C++/SystemC, which we believe is “The Easiest Path from ESL to Silicon”.
System-level designers can simply use C, C++, or SystemC to describe the system functionalities and behaviors, and these descriptions together with the user constraints can be directly passed to our AutoPilot synthesis tool.
AutoPilot goes through three major steps to synthesize the high-level untimed or partially-timed behavioral specifications to fully-timed RTLs.
Front-end compilation and elaboration to parse in your input design and analyze the semantics of the hardware-specific constructs in SystemC.
Advanced and aggressive code transformations to optimize the C/C++ or SystemC code.
Afterwards, we do core synthesis and optimizations. The synthesis process is platform-dependent and communication-centric. We consider both behavior and communications, and optimizes logics and interconnects simultaneously.
The outputs from AutoPilot include the RTL HDLs in either VHDL or Verilog and the timing/power/layout constraints to guide the downstream RTL synthesis and physical design tools. We also generate the RTL SystemC for simulation and verification. The idea is that we can use the same SystemC testbench to check the functional equivalence of the original C/System spec and the synthesized RTL.
Overall, AutoPilot delivers the following key benefits to the ESL designers.
It provides platform-based & communication-centric synthesis
It offers automated esl-to-gdsii silicon compilation
It helps rapid system-level “what-if” analysis and exploration
As a result, AutoPilot enables more than 10x design productivity gain

## Slide 34: We were also the First Users – E.g. Acceleration of Lithographic Simulation with AutoPilotTM
Lithography simulation
  Simulate the optical imaging process
  Computational intensive; very slow for full-chip simulation
15X+ Performance Improvement vs.
AMD Opteron 2.2GHz Processor with automated compilation
XtremeData X1000 development system (AMD Opteron + Altera StratixII EP2S180)
AutoPilotTM Synthesis Tool
Algorithm in C
I(x,y) = S lk * | S t [yk(x-x1, y-y1) -
yk(x-x2, y-y1) + yk(x-x2, y-y2) - yk(x-x1, y-y2)] |2
Notes: We’ve used AutoPilot to accelerate a lithographic aerial image simulation application, which is an essential component in most DFM (Design for Manufacturability) flows. The lithography simulation itself is a very computationally demanding process and often requires clusters with hundreds CPUs to achieve acceptable turn-around time.
The whole algorithm is written in 2226 lines of C code and synthesized by AutoPilot, which generates about 24K lines of VHDL code.
The accelerator has been implemented on XtremeData XD1000 development system. The development system uses a dual Opteron motherboard
and one of the Opteron processors is replaced by an XD1000 co-processor module. The XD1000 co-processor is built around an Altera Stratix II EP2S180. The FPGA co-processor communicates with the host Opteron CPU via the HyperTransport links.
To measure the performance speedup, we conduct experiments on a 200umx200um chip layout specified in GDSII format. The FPGA accelerated implementation runs 15x faster than the pure software implementation on an AMD Opteron 248 processor at 2.2GHz with a 4GB DDR memory.

## Slide 35: Needs for Automated Loop Transformations
Loop interchange
Loop over pixels
Loop over kernels
Loop over layout corners
Loop over kernels
Loop over layout corners
Loop over pixels
Different kernels do not have much correlation, thus put to the outer loop
Fix one specific layout corner, loop over pixels for more regular data access

## Slide 36: Need Automated Loop Unrolling
Loop unrolling is one option to express parallelism in those tools
The improvement by loop unrolling is limited due to port conflicts
  Data access of the same array cannot be scheduled to the same cycle due to port conflicts
  May increase the initial interval when both loop pipelining and loop unrolling is used
Loop unrolling

## Slide 37: Needs of Automated Memory Partitioning
Unrolling did not solve the problem completely due to port conflictions
Need a multi-port (on-chip) mem with a large number of ports!
  Implement the multi-port mem via memory partitioning
Computing tasks can be done in parallel once we get the multiple data in parallel
  Each PE is responsible for computing one partition of image
  Each PE composed of one partition of kernel and one partition of image partial sum
  Multiplexing logic gets the data from
  different partitions of kernel and provides
  the data for each PE
  To compute one partition of image,
  might also need the kernel data in
  other partitions
Kernel partition 1
Image
Partial Sum partition 1
Computing Element
Kernel partition 2
Image
Partial Sum partition 2
Computing Element
One partition
of Kernel
One partition of Image
Partial Sum
Computing Element
Kernel partition 4
Image
Partial Sum partition 4
Computing Element
Multi
plexing
Logic
4-PE example
Kernel partition 3
Image
Partial Sum partition 3

## Slide 38: Outcome: AutoPilot Became Highly Competitive
Metric | RTL Expert | AutoPilot Expert | Diff (%)
LUTs | 32,708 | 29,060 | -11%
Registers | 44,885 | 31,000 | -31%
DSP48s | 225 | 201 | -11%
BRAMs | 128 | 99 | -26%
E.g. Xilinx results before acquisition
Wireless MIMO Sphere Decoder
  ~4000 lines of C code
  Xilinx Virtex-5 at 225MHz
Compared to optimized IP
  11-31% better resource usage
TCAD April 2011 (keynote paper)
“High-Level Synthesis for FPGAs: From Prototyping to Deployment”
Notes: 38

## Slide 39: Concluding Remarks
I was very fortunate to have Bryan as my mentor in my internship at Xerox PARC
  Benefited immensely from Bryan’s vast experience, deep insight, and remarkable wisdom
  A long-term friendship
The truly important lesson that I learned from Bryan
  Go from design to design automation
  Gain first-hand knowledge and experience about needs from the designer’s perspective, to discover and formulate new EDA problems and develop impactful solutions.

## Slide 40: Guess Where This Picture Is Taken?