## Slide 1: Interconnect Length Estimation in VLSI Designs: A Retrospective
Massoud Pedram
University of Southern California

## Slide 2: Motivation and Problem Definition
Interconnect represents an increasingly significant part of total circuit delay
  Longer interconnect is more significant
Interconnect is accurately known only after place/route
  This leads to timing closure problems
  Logic design is now coupled with physical design
Interconnect must be considered during:
  Floorplanning, synthesis, timing verification
We need to be able to predict the length of individual wires before layout, say during technology mapping

## Slide 3: Previous Work
Previous work in this area:
  Pedram and Preas, ICCD-89
    Average wire length for given pin-count
  Heineken and Maly, CICC-96
    Wire-length distribution
  Hamada, Cheng, and Chau, TCAD 1996
    Average wire length for given pin-count
  Srinivas Bodapati, Farid N. Najm, TVLSI 2001
  Andrew Kahng and Sherief Reda, SLIP 2006
  Dirk Stroobandt
  Others …

## Slide 4: Key Ideas
The number of pins on a net (denoted Pnet) is known to affect net length
The first level neighborhood (denoted Nh1(i) ) of a given net i is defined as:
  The set of all other nets connected to cells to which this net is also connected
The second level neighborhood (denoted Nh2(i) ) of a given net i is defined as:
  The union of all first level neighborhoods of nets that are in the first level neighborhood of this net

## Slide 5: LEQA: Latency Estimation for a Quantum Algorithm Mapped to a Quantum Circuit Fabric
Mohammad Javad Dousti and Massoud Pedram
(DAC 2013 Paper)

## Slide 6: Related Papers
M. Pedram. B. T. Preas, "Accurate prediction of physical design characteristics of random logic," Proc. of Int'l Conference on Computer Design: VLSI in Computers and Processors, Oct. 1989, pp. 100-108.
M. Pedram. B. T. Preas, "Interconnection length estimation for optimized standard cell layouts," Proc. of Int’l Conference on Computer Aided Design, Nov. 1989, pp. 390-393.

## Slide 7: Overview
Introduction & Motivation
Problem Statement
Preliminaries
  Quantum Operation Dependency Graph (QODG)
  Universal Logic Blocks (ULBs)
Estimating the Latency of a Quantum Algorithm
  Average Routing Latency for CNOT Gate
LEQA Performance
Experimental Results
Conclusion

## Slide 8: Introduction & Motivation
Total execution time of a software depends on
  Processor architecture,
  Circuit design,
  Place and route.
Several estimation methods for the estimation of a software execution time without running it on a specific processor/processor simulator is proposed.
The same paradigm exists for quantum computers:
  Calculating the exact latency of a quantum algorithm is an expansive proposition since it needs scheduling and placement of quantum operations and routing of qubits
  The exact answer has no use since there is no real-size quantum computer out there!
  However, the latency estimation of the mapped quantum circuit still has many applications:
    Early algorithm/program analysis
    Helps quantum error correction code (QECC) designers to account enough amount of resources for QECCs

## Slide 9: Problem Statement
Given:
  A quantum circuit
  Size of the fabric (width×height)
  Logical gates delays
  The capacity of routing channels
  Speed of a logical qubit through the routing channels
Estimate the latency of the mapped quantum circuit to the quantum circuit fabric.

## Slide 10: Preliminaries (1): Quantum Operation Dependency Graph (QODG)
In QODG, nodes represent quantum operations and edges capture data dependencies.
QODG of ham3 circuit
Synthesized ham3 circuit
q1
q2
q3

## Slide 11: Preliminaries (2): Universal Logic Blocks (ULBs)
To avoid dealing with complexity, Tiled Quantum Architecture (TQA) is used which is composed of a regular two-dimensional array of ULBs.
A 3×3 Tiled Quantum Architecture (TQA)
Each ULB can perform any FT quantum operations.
ULBs are separated by the routing channels, which are needed to move logical qubits from some source ULBs to a target ULB in the TQA.
1
2
3
H
CNOT
T†
CNOT
T

## Slide 12: Estimating the Latency of a Quantum Algorithm
Delay of a quantum algorithm can be formulated as follows:
where
is the set of one-qubit FT operations (such as H, T, S, etc.);
and are the number of CNOTs and operations of type on the critical path;
and determine the delay of CNOT and operation of type respectively;
and capture the average routing latency for input qubits of the CNOT and the input qubit of the operation of type .
Tech, QECC, & QC dependent values
Easy; Empirically set to 2×Tmove
Main challenge!

## Slide 13
A computationally efficient model for estimating the average qubit routing latency for CNOT gates is developed.
The model comprises a number of sub-models dealing with
  Possible placement locations of each qubit captured as a “presence zone”
  Congestion in the routing channels captured by “zone overlaps”
  Intra-zone routing modelled as “shortest Hamiltonian path”
A procedural method, combining the sub-models together to estimate the Qubit routing latency for CNOT gates.
Average Qubit Routing Latency for CNOT Gate
Highly Congested
5 presence zones

## Slide 14: Estimating Average Routing Latency for CNOT (
Since the result of the placement is not known a priori, the zones are assumed to be placed randomly (uniformly and independently) on the fabric. can be estimated as
where
is the total number of logical qubits in the target quantum circuit;
is the expected area of the quantum circuit fabric which is covered by exactly overlapping presence zones;
is the average routing latency of a qubit when the routing channels are occupied by qubits; and
is the area of the circuit fabric and it is equal to the total number of ULBs assuming that each ULB is a square.
Should be estimated

## Slide 15: Estimating the Expected Covered Surface ()
where
is the probability that the ULB at position (x,y) on the fabric is covered by a qubit’s presence zone, which is itself randomly positioned on the fabric;
where
is the average area of presence zones.

## Slide 16: Estimating Average Area of Presence Zones (B)
A weighted graph called interaction intensity graph (IIG(V,E)) is built as follows:
  Nodes of this graph are logical qubits which are denoted by .
  An edge is added between nodes and if these two qubits interact with each other.
  is equal to the number of two-qubit operations between and .
Let denote the number of neighbors of node in the IIG(V,E). Clearly, .
B can be calculated by using a weighted average over the size of the presence zone of all logical qubits
The area of the presence zone associated with , which is denoted by , is calculated as

## Slide 17: Average Routing Latency of a Qubit ()
where
is the capacity of routing channels
is the average routing latency of a qubit where all routing channels are uncongested
Derivation of this comes next

## Slide 18: Derivation of the Average Routing Latency of a Qubit ()
Routing latency when can be modeled by an M/M/1/∞ queue. ( is the arrival rate)
Avg. Queue length:
Having the arrival rate and the avg. queue length, Little’s formula gives the average waiting time in the queue:

## Slide 19: Estimating
where represents the average routing latency of qubit in an average-size presence zone when the routing channels are uncongested.
One way to estimate is to randomly place qubits in the presence zone of qubit and calculate the expected length of the shortest Hamiltonian path () which goes through these qubits.

## Slide 20: Estimating
can be estimated
By knowing the value of , can be calculated as follows:
where is a tuning parameter and is a parameter depending on the physical characteristics of the fabric technology mostly the speed of moving a logical qubit through channels. is added to the denominator to give the average routing latency of an operation (i.e., a single edge length).

## Slide 21: LEQA Performance
Runtime complexity of LEQA can be written as follows:
where
is the number of vertices in the given QODG which is equal to the number of operations plus two (including two dummy nodes)
is the number of edges in the given QODG
is the number of qubits in the input circuit
is the area of the TQA fabric
Polynomial in terms of input size (operation count, qubit count and fabric size)

## Slide 22: Experimental Results (1)
LEQA is compared with a modified version of our previous work QSPR (DATE’12)
Average error is 2.11%
Worst case error; still low enough

## Slide 23: Experimental Results (2)
Shor’s factorization algorithm for a 1024-bit integer has ~1.35×1010 logical operations. Using extrapolation, QSPR would compute the latency in ~2 years whereas LEQA needs only 16.5 hours!!

## Slide 24: Conclusion
Persistence of Ideas
  The method developed some 25 years ago applies today not to classical computing but also to quantum computing fabric
Gratitude of Scholars
  We are who we are because of what we have learned from whom and what we have done since
Voice of Hearts
  Friendship and collegiality are key