## Slide 1
Shang-Tsung Yu, Sheng-Han Yeh, and Tsung-Yi Ho
jidung@eda.csie.ncku.edu.tw
http://eda.csie.ncku.edu.tw
Electronic Design Automation Laboratory
Department of Computer Science and Information Engineering
National Cheng Kung University
Tainan, Taiwan
Reliability-Driven Chip-Level Design for
High-Frequency Digital Microfluidic Biochips
ISPD 2014
Notes: Thanks for chair’s introduction.
Hello, everyone.
I’m Shang-Tsung Yu. I come from Taiwan and I am the student of NCKU in Taiwan.
I did this research with my senior Sheng-Han Yeh, and my advisor Tsung-Yi Ho.

## Slide 2: Outline
Introduction
Problem Formulation
Algorithm
Experimental Results
Conclusions
Notes: Here is my outline.
There are introduction, problem formulation, algorithm, experimental results and conclusions.

## Slide 3: Digital Microfluidic Biochips (DMFBs)
The architecture of DMFBs
  2D microfluidic array: A set of basic cells for biological reactions
  Droplets: Biological sample carrier as basic units to perform the laboratory procedures on a DMFB
  Reservoirs/dispensing ports: Generate droplets
  Optical detectors: Detection of reaction result
Notes: Higher throughput and smaller sample/reagent consumption
Compared with the traditional experimental platform
Portable devices for implementing the laboratory procedures in biochemistry

## Slide 4: Electrowetting-On-Dielectric Chips (EWOD Chips)
For EWOD chips, electrodes can be actuated by applying voltage to the electrode.
Side view
Droplet
Bottom plate
Top plate
Ground electrode
Control electrodes
Hydrophobic insulation
Actuated
Droplet
Generated electrical field
Notes: How does the Digital Microfluidic Biochip work ?
It utilizes a technology called Electrowetting-On-Dielectric chips.
We can see the sectional drawing. There are hydrophobic insulation layer, top plate, bottom, and control electrodes.
When the droplets are dispensed into the platform, it will be sandwiched between the top plate and the bottom plate.
By applying voltages to the electrodes, electrodes can be actuated, an electrical field is generated and droplets will move forward by natural phenomenon.
Thus, by applying time-varying voltages, we can perform biological operations I mentioned before.

## Slide 5: Operation of Digital Microfluidics (1/3)
Transport
25 cm/s flow rates, order of magnitude
Notes: 2D is also ok

## Slide 6: Operation of Digital Microfluidics (2/3)
Splitting/Merging

## Slide 7
Droplet Dispensing
Synchronization of many droplets
Operation of Digital Microfluidics (3/3)

## Slide 8: Chip-Level Design of EWOD Chips
Bottom layer contains conduction wires, electrical pads, and a substrate
The routing problem: 2D pin array (routing inner electrodes to outside electrical pads)
How to control these electrodes
Bottom Layer
Notes: Concern about

## Slide 9: Pin-Constrained EWOD chips
Huge number of electrodes in large-scale DMFBs
Limited number of ports in external controller
Broadcast addressing technique for pin-constrained
  - Reduce pin count and fabricate cost
Pin Count: 12
Pin Count: 5
Electrodes share the same control pin
Notes: Each electrode should be addressed by pins to apply voltage.
But the problem is

## Slide 10: Broadcast Electrode Addressing (1/2)
X
Electrode Actuation Sequence (AS)
  An AS represents every status demanded at each time step
  1: Actuated term
  0: Grounded term
  X: Don’t care term
Share the same control pin
  By observing, multiple electrodes can share an identical sequence by replacing X with 1 or 0
1
X
0
1
0
0
X
1
0
1
X
X
1
1
1
0
0
1
Compatible
time step | 1 | 2 | 3 | 4 | 5 | 6
status of electrode | 1 | 0 | X | 0 | 1 | X
These electrodes can be merged
into the same control pin
Notes: Before I talk about the detail in the broadcast addressing, let me introduce the electrode actuation sequence first.
To do a specific biological operation, each electrode has his own actuation sequence.
An actuation sequence represents every status demanded at each time step.
1 stands for actuated, 0 for grounded, and X for don’t care term.
By observing, we can know that some actuation sequences can share the same control pin by replacing don’t care terms with 0 or 1.
For example, these two actuation sequences, by replacing the don’t care term, we know that they are compatible.

## Slide 11: Broadcast Electrode Addressing (2/2)
Broadcast addressing constraint
  If the actuation sequences are (aren’t) mutually compatible, they can (cannot) be addressed with the same control pin
e1
e2
e3
e4
e5
e6
e7
e8
e9
e10
e11
e12
Electrode groups: {e1 , e2 , e9 , e10}, {e3 , e4 , e5 , e8 , e11 , e12}, {e6 , e7}
Pin 1
Pin 2
Pin 3
e1
e2
e3
e4
e5
e6
e7
e8
e9
e10
e11
e12
Compatibility graph
Clique
partition
Electrode
Compatible
Notes: To implement broadcast addressing, we will build a graph.
It is called compatibility graph.
A node stands for an electrode, and an edge stands for compatible relationship.
For example, we can see that electrode 2 is compatible with electrode 10.
In fact, in the view of this graph, doing broadcast addressing is the same as doing clique partition on this graph.
All electrodes in a clique can be controlled by a pin because all of them are mutually compatible.

## Slide 12: Reliability Issue (1/2)
Arbitrary broadcast addressing will cause huge number of switching times in resulting AS
e1
e2
e3
10X0X0
1X0X00
X01X1X
101010
Number of switching times () = 5
100000
Number of switching times () = 1
e1
e2
e1
e3
Notes: However, arbitrary broadcast addressing will cause huge number of switching times.
For example, e1 and e2 are compatible. e1 and e3 are also compatible.
If e1 and e3 share the same pin, there are five switching times in the resulting actuation sequence.
If e1 and e2 share the same pin, there is one switching, which is a good result.

## Slide 13: Reliability Issue (2/2)
Contact angle reduction problem [10]
  High switching times will cause contact angle change reduction, and it will decrease the reliability especially in high frequency DMFB.
[10] L. Huang, B. Koo, and C. J. Kim, Evaluation of anodic Ta2O5 as the dielectric layer for EWOD devices," IEEE MEMS, pp. 428-431, 2012.
Grounded
Actuated
The reliability issue can be modeled as
  Maximum of switching times ()
Notes:   In order to minimize the time required to complete a bioassay, a high-frequency DMFB is needed

## Slide 14: Outline
Introduction
Problem Formulation
Algorithm
Experimental Results
Conclusions
Notes: Then, we enter into problem formulation.

## Slide 15: Problem Formulation
Input
  Chip size: m x n
  Electrode set: (their locations)
  Actuation sequence of each electrode (ex: “0010X”)
  Pin constraint
Goal & Constraint
  Minimize the value of
  Meet all the design constraints
    Broadcast addressing constraint
    Pin constraint
    Wire routing constraint
Output
  A feasible electrode addressing solution and wire routing solution
Notes: The location of electrode, the actuation sequence AS and the pin constraint P_max are given.

## Slide 16: Outline
Introduction
Problem Formulation
Algorithm
Experimental Results
Conclusions
Notes: Here we goes to algorithm.

## Slide 17: Algorithm
The algorithm contains 2 main steps
Step 1. Incremental search
Step 2. Simultaneous broadcast addressing and routing
Notes: There are totally two main steps.
Incremental search and simultaneous broadcast addressing and routing.

## Slide 18: Incremental Search Method (1/4)
  Lower Bound of Switching Times (BST)
XX0X111XXX001X01
011100101
eliminate X terms
Notes: Before talking about the algorithm, let’s introduce the lower bound of switching times.
It is defined as BST.
It can be easily computed by eliminating all the don’t care terms.
For example, the BST of this actuation sequence is 5.
That is, after finishing the broadcast addressing, its number of switching times will be greater or equal than 5.
By induction, the maximum of number of switching times is greater than or equal to the maximum of BST.

## Slide 19: Incremental Search Method (2/4)
Switching-constrained compatibility graph under a specific value
  An edge was constructed between two electrodes a & b when their switching times is not greater than after merging
e1
e2
e3
10X0X0
1X0X00
X01X1X
100000
(ST=1)
Smax = 3
Smax = 5
101010
(ST=5)
Notes: To minimize the switching times caused by broadcast addressing, we define a S_max which is the switching-constrained.
That is, we don’t allow the switching times is bigger than this value when we are doing the broadcast addressing.
The switching-constrained compatibility graph is the compatibility graph under the switching-constraint of a specific value S_max.
It is called Gscc.
For example, when Smax is equal to 5, these two edges in the Gscc are allowed.
However, if the Smax is equal to 3, the edge will be abandoned even though they are compatible in their actuation sequence.
Because its number of switching times is bigger than 3.

## Slide 20: Incremental Search Method (3/4)
A value (start from lower bound ) is gradually increasing by 1 for each iteration
Construct switching constrained compatibility graph Gscc under
Simultaneous broadcast
addressing and routing
Smax += 1
NO
YES
A feasible solution
Feasible solution?
Notes: So, we can talk about incremental search.
We want to search feasible Smax and keep it as small as possible.
Start from BST_max, construct switching constrained and execute the simultaneous broadcast addressing and routing.
When there is no feasible solution, the Smax is added by one.

## Slide 21: Incremental Search Method (4/4)
  If we can find a feasible solution under , then we can obtain a solution with
high
low
ST
infeasible
feasible
infeasible
Notes: If we can find a feasible solution under , then we can obtain a solution with .
So we can get a feasible solution with better reliability.
If we can find a feasible solution under 𝐺_𝑠𝑐𝑐, then we can obtain a solution with 〖𝑆𝑇〗_𝑚𝑎𝑥≤𝑆_𝑚𝑎𝑥.
So we can get a feasible solution with better reliability.

## Slide 22: Simultaneous Broadcast Addressing and Routing (1/2)
Main idea: progressive solving
Divide the original problem into a set of manageable sub-problems
corresponding to a pin-electrode merging
: Unaddressed electrodes
: Addressed electrodes
e8
e2
e3
e4
e6
e7
e1
e10
e9
e5
e1
e2
e3
e4
e8
e7
e6
e5
e10
e9
e5
e1
e8
e10
e10
e5
e8
e1
e2
e3
e6
e7
Set initial pins by a maximal independent set
Broadcast addressing and routing
e2
e3
e6
e7
e4
Set an unaddressed electrode as a new pin
e4
Broadcast addressing and routing
e9
e9
P2
P1
P3
P4
P5
Switching-constrained compatibility graph
Broadcast addressing and routing
Notes: The wire routing between e3 and p1 will be conducted simultaneously
Assuming that the wire routing between e4 and p2 failed, e4 cannot be added into p2 even though they are mutually compatible

## Slide 23: Simultaneous Broadcast Addressing and Routing (2/2)
Simultaneous broadcast
addressing and routing
Construct switching constrained compatibility graph Gscc under
Simultaneous broadcast
addressing and routing
Smax += 1
NO
YES
A feasible solution
Feasible solution?
Identify an initial electrode set and
address them with individual control pins
Find pin-electrode candidates by
network flow model
NO
1. Trace the resulting flow
2. Routing check and conduct the broadcast addressing and routing
Do escape routing and output the solution
All electrodes are addressed?
YES
Notes: So, we can talk about incremental search.
We want to search feasible Smax and keep it as small as possible.
Start from BST_max, construct switching constrained and execute the simultaneous broadcast addressing and routing.
When there is no feasible solution, the Smax is added by one.

## Slide 24: Network Flow Model (1/2)
Minimum-Cost Maximum-Flow (MCMF) formulation
  To find suitable merging candidates between and
Existed control pins
Unaddressed electrodes
‧‧‧
‧‧‧
P1
P2
Pn-1
Pn
S
T
UE1
UE2
UEm-1
UEm
Capacity = 1
Cost = 0
Capacity = 1
Cost = 0
Capacity = 1
Cost = HPWL-Extension( Pi , UEj )
Gscc
Notes: Here is our network flow model.
Pins, Unaddressed electrodes, source, sink.
Edges between pins and unaddressed electrodes are built according to the Gscc.
We set capacity of each edge as 1, and cost as HPWL-Extension which can estimate routing cost.
We use the MCMF to help us get suitable pin-electrode merging pairs.
The intention of this model is using lower routing cost to do the progressive broadcast addressing.
When there is a resulting flow from S, P1, UE2, T, we will take the P1 UE2 merging into consideration.
Do wire routing check. If it is a successful routing, then do the merging.

## Slide 25: Network Flow Model (2/2)
HPWL-Extension
  The variation of half-perimeter wire length
  (The variation of half-perimeter of bounding box)
Cost = 3
Cost = 0
Using lower routing cost to do the broadcast addressing and routing
Notes: The intention of this model is using…

## Slide 26: Wire Routing
Pin-electrode merge
  Only if there is a successful routing between a pin and an electrode, they can be merged
e1
e2
e8
routing check
P1
Two-stage routing check will be conducted one by one from candidates
candidate 1
candidate 2
candidate 3
Notes: As mentioned before, we progressively conduct pin-electrode merge.
For example, after a round of network flow, we derives 3 matching candidates from the result of network flow.
Nets of merge should be routed by conduction wires.
However, not every routing will be successful.
So, two-stage routing check will be conducted.

## Slide 27: Wire Routing Check
Stage 1: Do wire routing check between existing pin and unaddressed electrode from candidates
Wire routing check failed because can NOT reach the pin
If is going to be merged with a pin containing and , a wire routing check is conducted by BFS algorithm
Drop this pin-electrode merging!
Notes: Stage 1: Do wire routing check whenever merging existing pin and unaddressed electrode
If is going to be merged with a pin containing and , a wire routing check is conducted.
For this example, wire routing check failed because can NOT reach the pin.
If this situation happen, we drop this pin-electrode merging.
Stage 1: Do wire routing check whenever merging existing pin and unaddressed electrode
If 𝑒_5 is going to be merged with a pin containing〖 𝑒〗_6 and 𝑒_7, a wire routing check is conducted.
For this example, wire routing check failed because 𝑒_5 can NOT reach the pin.
If this situation happen, we drop this pin-electrode gerging.

## Slide 28: Escape Routing Check
Stage 2: Do escape routing check whenever a wire routing check (stage 1) is successful
Escape routing check failed because and can NOT escape simultaneously without overlapping
(implemented by maximum flow)
Drop this pin-electrode merging!
Although the wire routing check between and is successful…
Escape routing
Wire routing
Notes: Stage 2: Do escape routing check whenever a wire routing check (stage 1) is successful.
Although the wire routing check between and is successful…
Escape routing check failed because and can NOT escape simultaneously without overlapping.
That is, if e5 and e7 don’t share the same control pin finally.
They cannot do escape routing independently.
Drop this pin-electrode merging!
That is, only when both stage 1 and stage 2 routing checks are approved, we will really do the pin-electrode merging.
By doing this, we can keep the feasible routing solution when we are doing the broadcast addressing.
Stage 2: Do escape routing check whenever a wire routing check (stage 1) is successful.
Although the wire routing check between 𝑒_3 and 𝑒_4 is successful…
Escape routing check failed because 𝑒_5 and 𝑒_7 can NOT escape simultaneously without overlapping.
Drop this pin-electrode merging!

## Slide 29: Conduct the Merging and Routing Successfully
If both the stage 1 and stage 2 checks are approved, conduct the merging and routing immediately
e1
e2
e8
routing check
P1
e8
P1
e1
e2
candidate
e8
conduct routing
Notes: Stage 2: Do escape routing check whenever a wire routing check (stage 1) is successful.
Although the wire routing check between and is successful…
Escape routing check failed because and can NOT escape simultaneously without overlapping.
That is, if e5 and e7 don’t share the same control pin finally.
They cannot do escape routing independently.
Drop this pin-electrode merging!
That is, only when both stage 1 and stage 2 routing checks are approved, we will really do the pin-electrode merging.
By doing this, we can keep the feasible routing solution when we are doing the broadcast addressing.
Stage 2: Do escape routing check whenever a wire routing check (stage 1) is successful.
Although the wire routing check between 𝑒_3 and 𝑒_4 is successful…
Escape routing check failed because 𝑒_5 and 𝑒_7 can NOT escape simultaneously without overlapping.
That is, if e5 and e7 don’t share the same control pin finally.
They cannot do escape routing independently.
Drop this pin-electrode merging!
That is, only when both stage 1 and stage 2 routing checks are approved, we will really do the pin-electrode merging.
By doing this, we can keep the feasible routing solution when we are doing the broadcast addressing.

## Slide 30: Matching Pairs in Order
To have more pairs of successful routing, matching pairs (candidates) will be checked for routing and route in the increasing order of their cost ()
P1
P2
P3
P4
S
T
UE1
UE2
UE3
UE4
UE5
P5
7
9
12
5
20
Order:
1. - (5)
2. - (7)
3. - (9)
4. - (20)
Notes: Stage 2: Do escape routing check whenever a wire routing check (stage 1) is successful.
Although the wire routing check between and is successful…
Escape routing check failed because and can NOT escape simultaneously without overlapping.
That is, if e5 and e7 don’t share the same control pin finally.
They cannot do escape routing independently.
Drop this pin-electrode merging!
That is, only when both stage 1 and stage 2 routing checks are approved, we will really do the pin-electrode merging.
By doing this, we can keep the feasible routing solution when we are doing the broadcast addressing.
Stage 2: Do escape routing check whenever a wire routing check (stage 1) is successful.
Although the wire routing check between 𝑒_3 and 𝑒_4 is successful…
Escape routing check failed because 𝑒_5 and 𝑒_7 can NOT escape simultaneously without overlapping.
That is, if e5 and e7 don’t share the same control pin finally.
They cannot do escape routing independently.
Drop this pin-electrode merging!
That is, only when both stage 1 and stage 2 routing checks are approved, we will really do the pin-electrode merging.
By doing this, we can keep the feasible routing solution when we are doing the broadcast addressing.

## Slide 31: Blacklist of Failed Routing Pairs
Record those pin-electrode matching pairs (candidates) with failed routing check into the blacklist
When the is rebuilt for the following network flow model, the edges in the blacklist will NOT be built again.
P1
P2
P3
P4
S
T
UE1
UE2
UE3
UE4
UE5
Blacklist:
-
-
-
-
P5

## Slide 32: Review Algorithm
Calculate Lower Bound of
Switching Times
Set Initial Switching-Constrained
Construct
Compatibility Graph
Select an Initial Pin Set
Resulting Flow = 0 ?
NO
Build MCMF Network Flow Model
YES
Routing Check, Merge Pins and Electrodes and Conduct Wire Routing
Rebuild Compatibility Graph
# of Unaddressed Electrodes = 0 ?
YES
Select an Unaddressed Electrode as a New Pin
NO
YES
Meet Pin-Constrained ?
End
Switching-Constrained = Switching-Constrained + 1
NO
Abandon Current Matching Results
Notes: So, we can talk about incremental search.
That means the network flow get stuck.
We want to search feasible Smax and keep it as small as possible.
Start from BST_max, construct switching constrained and execute the simultaneous broadcast addressing and routing.
When there is no feasible solution, the Smax is added by one.

## Slide 33: Outline
Introduction
Problem Formulation
Algorithm
Experimental Results
Conclusions

## Slide 34: Experimental Result (1/3)
Environmental Setup
  CPU: Intel(R) Core(TM) i7-3770 CPU @ 3.40GHz
  Memory: 8GB DDR3-1600
  Operating System: Linux Mint 15 Olivia with 64-bits
  Programming Language: C++
5 real-life chips are used for test cases
Chip | Size | #E | Pmax | #Time Step | BST
amino | 6 X 8 | 20 | 16 | 34 | 12
Multiplex | 15 X 15 | 59 | 32 | 20 | 4
PCR | 15 X 15 | 62 | 32 | 20 | 6
Multifunctional | 15 X 15 | 91 | 64 | 77 | 12
DNA preparation | 13 X 21 | 77 | 32 | 106 | 12
Notes: There are 5 real-life chips used for test cases
What we focus is the bound of switching times.

## Slide 35: Experimental Result (2/3)
Chip | Baseline |  |  |  | Ours |  |  | 
 |  | #Pin | GR(%) | CPU |  | #Pin | GR(%) | CPU
amino | 14 | 13 | 16.67% | 0.19 | 12 | 14 | 0% | 0.15
multiplex | 10 | 18 | 150% | 29.6 | 4 | 23 | 0% | 21.95
PCR | 12 | 29 | 100% | 33.2 | 6 | 32 | 0% | 34.09
multifunctional | 16 | 58 | 33.33% | 39.8 | 12 | 61 | 0% | 37.62
DNA preparation | 22 | 28 | 83.33% | 41.5 | 13 | 31 | 8.33% | 70.78
Chip | Baseline |  |  |  | Ours |  |  | 
 |  | #Pin | GR(%) | CPU |  | #Pin | GR(%) | CPU
amino | 14 | 13 | 16.67% | 0.19 | 12 | 14 | 0% | 0.15
multiplex | 10 | 18 | 150% | 29.6 | 4 | 23 | 0% | 21.95
PCR | 12 | 29 | 100% | 33.2 | 6 | 32 | 0% | 34.09
multifunctional | 16 | 58 | 33.33% | 39.8 | 12 | 61 | 0% | 37.62
DNA preparation | 22 | 28 | 83.33% | 41.5 | 13 | 31 | 8.33% | 70.78
*Growth Rate (GR):
Notes: Baseline is generated without considering the switching times and it is just for comparison.
It is obviously that the stmax is very bad in baseline.
You can see in ours result, there are 4 cases whose Stmax is the same as bound of switching.
That is the growth rate is 0 %.
Only the GR of DNA preparation is not 0%.
It is because that the pin-constrained is very tight.
That is, maybe DNA preparation need 33 pins or 34 pins so that it can get 12 Stmax.

## Slide 36: Experimental Result (3/3)
Result of multifunctional assay
Size: 15x15
#Electrode: 91
Pmax: 64
#Pin: 64
: 0%
Notes: Here, we show the addressing and wire routing result of the multi-
functional chip which has the largest number of electrodes
among all test cases.

## Slide 37: Outline
Introduction
Problem Formulation
Algorithm
Experimental Results
Conclusions

## Slide 38: Conclusions
Reliability-driven chip-level design for high-frequency DMFB
A network flow based progressive addressing to handle the complex problem
The contact angle reduction problem is minimized.
Notes: Conclusions

## Slide 39
Thank You !
Any Question ?

## Slide 40: Appendixes Motivation for Microfluidic Biochips
Applications: Clinical diagnostics, environmental monitoring, automated drug discovery, etc.
Test tubes
Automation
Integration
Miniaturization
Robotics
Automation
Integration
Miniaturization
nl-pl sample
Microfluidics Biochips
Automation
Integration
Miniaturization
Higher throughput, minimal human intervention,
smaller sample/reagent consumption
Notes: In recent years, microfluidic biochips are receiving much attention. These microsystems are also known as lab-on-chips or bioMEMS. They have roughly the size of a coin. Compared to the conventional biochemical analyzer, they have many advantages,such as smaller size, lower cost and higher sensitivity. A promising application area for microfluidic biochips is clinical diagnostics, such as health care for premature infants. And also, these biochips can perform automatic bimolecular detection. So they can be used as bio-smoke alarm to counter bioterrisiom. In addition, these biochips can serve as a platform for massive parallel DNA analysis or drug discovery.
Hemophilia
Urine

## Slide 41: Appendix Broadcast Electrode Addressing
Droplet
Spacing
High voltage to generate an electrical field
0
0
1
0
X
X
X
time
X
0
0
1
0
X
X
X
X
0
0
1
0
X
X
X
X
0
0
1
0
X
X
X
X
0
0
1
Wire
External controller
Actuation sequence
0
0
X
X
X
0
0
X
X
X
1
0
0
1
0
1
0
0
1
0
0
1
0
0
1
0
1
0
0
1
7 pins -> 4 pins
Broadcast addressing
Electrode
impossible
Notes: Introduce the actuation sequence and then the mechanism of broadcast-addressing scheme

## Slide 42: Appendixes CAD Flow (1/2)
Sequencing Graph
Microfluidic Module Library
Design Spec.
Architectural-Level
Synthesis
Scheduling
Resource Binding
O1
O2
Resource | Area | Time
Mixer | 2x2-array | 7
Mixer | 1x3-array | 4
LED | 1x1 cell | 10
Storage | 1x1 cell | N/A
O3
O4
O5
O6
Store
Dispense
Store
Mix
Mix
Detection
Operation | Resource
O1 | On-chip
O2 | 2x2-array
O3 | 1x1 cell
O4 | LED
O5 | 1x3-array
O6 | 1x1 cell
Max. Area: 5x5 array
Max. Completion Time: 50 seconds
O1
O3
O6
O5
O2
O4

## Slide 43: Appendixes CAD Flow (2/2)
Scheduling
Resource Binding
Operation | Resource
O1 | On-chip
O2 | 2x2-array
O3 | 1x1 cell
O4 | LED
O5 | 1x3-array
O6 | 1x1 cell
Placement
 | O2 |  |  | O1
O4 |  |  | O5 | 
 |  | O6 |  | O3
Physical-Level
Synthesis
Routing
 | O2 |  |  | O1
O4 |  |  | O5 | 
 |  | O6 |  | O3
O1
O3
O6
O5
O2
O4