## Slide 1: Design Synthesis and Optimization for Automotive Embedded Systems
Qi Zhu
University of California, Riverside
ISPD 2014
April 2, 2014
Notes: Synthesis is more on the software side

## Slide 2: More Intelligent Vehicles – Active and Passive Safety
by Leen and Effernan – IEEE Computer
Notes: Trend: more intelligent, from passive safety to active safety
This is being driven by the advancement of the automotive embeddedsystems

## Slide 3
LDW wil warn the driver if he or she is on the verge of inadvertently drifting out of the lane. Using a CMOS Camera and an image processing algorithm, this driver assistance system registers the course of the lane in relation to the vehicle. The system "sees", as it were, the course of the road and where the car is going. If the warning algorithm detects an imminent leaving of the current driving lane, the system warns the driver with haptic, kinestatic, or acoustical feedback. Possible warning alerts can be a trembling in the steering wheel, a vibrating seat or a virtual washboard sound. Production from 2005.
(Source: Continental website)
Active Safety Example – Lane Departure Warning (LDW)

## Slide 4: Challenges in Automotive: Electronics and Software Shifting the Basis of Competition
Value from Electronics & Software
ABS: Antilock Brake System
ACC: Adaptive Cruise Control
BCM: Body Control Module
DoD: Displacement On Demand
ECS: Electronics, Controls, and Software
EGR: Exhaust Gas Recirculation.
GDI: Gas Direct Injection
OBD: Onboard Diagnostics
TCC: Torque Converter Clutch
PT: Powertrain
Forefront of Innovation
Vehicle Integration
System Connection
Subsystem Controls & Features
Hybrid PT
EI
ACC
Rear Vision
Passive Entry
Side Airbags
Fuel Cell
Wheel Motor
…
OnStar
OBD II
HI Spd Data
Rear aud/vid
CDs
BCM
ABS
TCC
EGR
Electric Fan
Head Airbags
...
Electric Brake
DoD
GDI
…
…
…
…
…
…
1970s
1980s
1990s
2000s
2010s
2020s
$1182 (+196%)
50 ECUs (+150%)
100M Lines of Code (+9900%)
$400
20 ECUs
1M LOC
~
~
More electronics and software
More distributed, more contention
90% of all future innovations will be on electronics systems
Mechanical $
Electronics $
55%
24%
Other $
Software $
13%
8%
AVG.
Software $
Mechanical $
76%
Other $
Electronics $
13%
9%
2%
AVG.

## Slide 5: More Distributed System, More Sharing Among Functions
Speed-dependant volume
Onstar emergency notification
Body
HVAC
ACC
Pre-2004
Stabilitrak 2
function6
function5
to 2010/12
to 2012/14
Post-2014
function17
Telematics
Transmiss.
Engine
Occupant Information
Exterior lighting
Occupant
protection
Infotainment
Environment sensing
Object detection
Suspension
Steering
Brake
Subsystem
function7
function8
function9
function10
function11
function12
function13
function14
function15
function16
Courtesy: GM Research

## Slide 6: Automotive Security

## Slide 7: Challenges in Automotive: Methodologies and Tools
More problems in vehicle electronic systems:
  50% of warranty costs related to electronics and software.
  Recalls related to electronic systems tripled in past 30 years.
  Hard to diagnose: more than 50% of the ECUs replaced are technically error free.
Methodologies and tools are needed for
  Modeling, analyzing and verifying complex system behavior with formal models.
  Synthesizing models to implementation while maintaining functional correctness and optimizing non-functional metrics such as performance, reliability, cost, security, energy, extensibility.
  Addressing multicore and distributed platforms.
Notes: What these trends lead to … more problems and need of more methodologies and tools

## Slide 8: AUTOSAR Architecture
AUTOSAR SW-C 1
SW-C Description
Virtual Functional Bus
Basic Software
RTE
AUTOSAR SW-C 1
ECU1
AUTOSAR SW-C 2
SW-C Description
AUTOSAR SW-C 3
SW-C Description
AUTOSAR SW-C n
SW-C Description
ECU Descriptions
System Constraint Description
Deployment tools
Gateway
Basic Software
RTE
AUTOSAR SW-C 2
ECU2
AUTOSAR SW-C 3
Basic Software
RTE
AUTOSAR SW-C n
ECU3
Notes: Automotive community has been trying to address such challenges.
AUTOSAR (AUTomotive Open System ARchitecture) is an open and standardized automotive software architecture, jointly developed by automobile manufacturers, suppliers and tool developers.

## Slide 9: Typical Automotive Supply Chain
Suppliers
OEMs
AUTOSAR component protecting IP
SR (Simulink) models
Task code
From functional models to runnable (code) implementations, to task models deployed onto architecture platform.
(courtesy: Fabio Cremona)
Notes: Separation of concerns also dictated by the supply chain model:…

## Slide 10: Functional model
f1
f2
f3
f4
f5
f6
s4
s5
s2
s3
s1
Functional model
deadline
Jitter constraint
function
period
activation mode
signal
period
is_trigger
precedence
Input interface
Output interface
Notes: Technically, what is the problem here:

## Slide 11: Architecture model
f1
f2
f3
f4
f5
f6
s4
s5
s2
s3
s1
ECU2
ECU1
ECU3
OSEK1
CAN1
Functional model
Architecture model
ECU
clk speed (Mhz)
register width
bus
speed (b/s)

## Slide 12: Mapping
f1
f2
f3
f4
f5
f6
s4
s5
s2
s3
s1
ECU2
ECU1
ECU3
OSEK1
CAN1
task1
task2
task3
task4
Functional model
Software tasks model
SR1
msg1
msg2
task
period
priority
WCET
activ.mode
message
CANId
period
length
transm. mode
is_trigger
resource
WCBT
Architecture model

## Slide 13: Model-Based Design and Synthesis
Software Tasks Model
Architecture Model
CPU 1
CPU 2
CPU k
…
Functional Model
Task mapping
Task gen.

## Slide 14: Automotive Design Requirements
Primary | Secondary | What is captured | Metrics unit
Performance/ Time | End-to-end latency | time distance between two events (related to stability and performance) | milliseconds
 | Jitter | maximum delay of a periodic signal with respect to ideal reference | milliseconds, or % of period,
 | Input coherency | time distance between two events/samples from multiple sensors observing the same object/phenomenon | milliseconds
Dependability | Reliability | expectation on failure, related to warranty cost impact | expected time between failures MTTF or fault rate (number of faults per hour)
 | Availability | percentage of uptime | MTTF/(MTTF+MTTR)
 | Safety | which faults can be tolerated and which cannot. Related to fault tolerance, fail safe vs fail operational | number of components/cutset that must fail for the system to fail
 | Extensibility | room for functional additions (e.g. Complement to resource utilization) | fraction of resource utilization available for future use
Cost |  |  | 
 | Piece cost (life cycle cost) |  | $
 | Degree of Reuse | ability to design/deploy using preexisting solutions, (SW or HW components, schedules and configurations) | number of units deployed
 | Scalability | suitability for a range of content level (while cost-effective) | number of programs or product lines

## Slide 15: Task Generation from Functional Model
Synchronous Reactive Semantics
Stateflow (FSMs) block
Dataflow block

## Slide 16: Multi-task Generation of Synchronous Finite State Machines
S1
S2
1 : e1 / a1
0.25ms
S3
2 : e2 / a2
0.2ms
4 : e2 / a4
0.5ms
3 : e1 / a3
0.3ms
e1: 2ms
e2: 5ms
1
2
S1
S2
1 : e1 / a1
0.25ms
S3
3 : e1 / a3
0.3ms
S1
S2
S3
2 : e2 / a2
0.2ms
4 : e2 / a4
0.5ms
(b) Multi-task implementation
(a) Single task implementation
Task Period: 1ms
Task Period: 2ms, 5ms
e1: 2ms
e2: 5ms
1
2

## Slide 17: Multi-task Generation of FSMs
(a) Original FSM
(b) Partitioned model based on events
(c) Mixed-Partitioned model
4-cycle conflicts

## Slide 18: General Partitioned Model
…
S1
S2
1 : e1 / a1
5 : e2 / a5
0.4ms
0.4ms
S3
2 : e2 / a2
0.2ms
1
2
1
2
4 : e2 / a4
0.5ms
3 : e1 / a3
0.3ms
e1: 2ms
e2: 3ms
Partition is valid as long as there are no cycles
T2: 1ms
T1: 1ms
T2: 3ms
T1: 1ms
T2: 1ms
T1: 2ms

## Slide 19: FSM Task Implementation Optimization
Design space
  Map transitions in each FSM F to a set of tasks
  Assign priorities to all tasks
Design objectives
  Breakdown factor
    Maximum factor λ that the execution time of all actions may be scaled by λ while maintaining system schedulability
  Action extensibility
    For each action a, the maximum factor a that the execution time of a may be scaled by a while maintaining system schedulability
    System action extensibility is a weighted average of each action’s extensibility.
[ Qi Zhu, Peng Deng, Marco Di Natale and Haibo Zeng, “Robust and Extensible Task Implementations of Synchronous Finite State Machines”, DATE 2013. ]

## Slide 20: Task Generation of Macro Dataflow Blocks (Synchronous Block Diagram)

## Slide 21: System-level Mapping for Distributed Automotive Embedded Systems
Functional Model
Architectural Model
- Allocation
Signal to Message
Priority
Period
……
- Latency
Utilization
……
Modeling
Design Space Exploration
ECU1
ECU2
ECU3
ECU4
BUS1
BUS2
IR
Sensor
Wheel
Sensor
Fusion
Task
Object
ID Task
Brake
Actuator
Nav.
Task
Signals
Mapping
Objectives and
Constraints

## Slide 22: Model-Based Design and Synthesis
Software Tasks Model
Architecture Model
CPU 1
CPU 2
CPU k
…
Functional Model
Task mapping
Task gen.

## Slide 23: Task Mapping onto Distributed Platform
Problems | 1: Allocation & Priority Assignment | 2: Period Assignment | 3: Extensibility Optimization
Design Variables | Allocation, Priority, Signal Mapping | Period | Allocation, Priority, Signal Mapping
Objective | Latency | Latency | Extensibility
Approach | Mixed integer linear programming (MILP) | Geometric programming (GP) | MILP & Heuristic
Address metrics: end-to-end latency and system extensibility.
Based on mathematical programming and heuristics.
Challenges: formulation and efficiency.
Focus on analytical worst case analysis for CAN-based systems with periodic tasks and messages.

## Slide 24: Task Allocation and Priority Assignment
T4
T2
T1
T5
T7
T3
T6
S1
S2
S3
S4
S5
S6
M1
M2
M3
Function
Model
Architecture
Model
10ms
20ms
20ms
20ms
20ms
40ms
20ms
20ms
40ms
100ms
40ms
40ms
20ms
300ms
1
2
1
3
2
1
2
3
1
2
ECU1
ECU2
ECU3
BUS1
BUS2
Task to ECU
Signal packing
Message to bus
Priority

## Slide 25: Two-step Algorithm Flow
Step1:
Assign task allocation
(using MILP)
Step2:
Assign signal packing, task and message priorities
(using MILP)
Constraints:
End-to-end latency on given paths
Utilization bound on ECUs and buses
Objective:
Sum of latencies on given paths
Design inputs:
Task worst case execution times
Signal lengths
Task and signal periods
Architecture topology, bus speeds
Heuristic:
Task and signal priorities
[Wei Zheng, Qi Zhu, Marco Di Natale and Alberto Sangiovanni-Vincentelli, “Definition of Task Allocation and Priority Assignment in Hard Real-Time Distributed Systems”, RTSS 2007. ]
[Qi Zhu, Haibo Zeng, Wei Zheng, Marco Di Natale and Alberto Sangiovanni-Vincentelli, “Optimization of Task Allocation and Priority Assignment in Hard Real-Time Distributed Systems”, ACM TECS, 2012]

## Slide 26: Security-Aware Task Mapping for CAN-based Distributed Systems
When retrofitting CAN architectures with security mechanisms, MACs (message authentication codes) may be added to CAN messages to protect against masquerade and replay attacks.
However, adding MAC bits to a design may not lead to optimal or even feasible systems due to limited CAN message sizes and timing constraints.
In this work, we designed an optimal MILP formulation and a heuristic for optimizing task allocation, signal packing, MAC key sharing, and priority assignment, while meeting both the end-to-end latency constraints and security constraints.
[Chung-Wei Lin, Qi Zhu, Calvin Phung, Alberto Sangiovanni-Vincentelli, “Security-Aware Mapping for CAN-Based Real-Time Distributed Automotive Systems”, ICCAD 2013]

## Slide 27: Summary
Model-based synthesis for automotive embedded systems
  Functional model with different semantics: FSMs, dataflow, heterogeneous and hierarchical models.
  Multicore and distributed architecture platform.
  Task generation and task mapping need to be addressed in a holistic framework.
    Functional correctness (affected by timing).
    Other non-functional requirements on performance, reliability, power, thermal, security, extensibility, etc.

## Slide 28: Problem 1: Allocation & Priority Assignment
T4
T2
T1
T5
T7
T3
T6
S1
S2
S3
S4
S5
S6
M1
M2
M3
Function
Model
Architecture
Model
10ms
20ms
20ms
20ms
20ms
40ms
20ms
20ms
40ms
100ms
40ms
40ms
20ms
300ms
1
2
1
3
2
1
2
3
1
2
ECU1
ECU2
ECU3
BUS1
BUS2
Task to ECU
Signal packing
Message to bus
Priority

## Slide 29: Experimental Results
Mapping
Using MILP based synthesis
(single-bus option)
Initial: total latency > 24000 ms, do not satisfy E2E latency constraints.
After Step1: total latency = 12295 ms, satisfy all constraints.
After Step2: total latency = 4928 ms.
...
ECU1
ECU2
...
ECU20
ECU21
...
...
ECU61
ECU62
Function Model
41 Tasks
83 Signals
171 paths with 100ms to 300ms deadlines
Architecture Model
9 ECUs
single-bus or dual-bus
Active safety application in GM experimental vehicle.

## Slide 30: Problem 2: Period Assignment
Design variables are task and message periods.
Allocation and priorities of tasks and messages are given.
Utilization and end-to-end latency constraints.
Approximate the
ceiling function
Geometric Programming
Task worst case response time:

## Slide 31: Iterative Algorithm Flow
Iteratively change αi
Parameters
  maxIt – max. # iterations
  errLim – max. permissible relative error between r and s
Start
all αi = 1;
ItCount = 0;
ItCount++;
(s, t) = GP(α);
Calculate r;
ei = (si – ri)/ri;
max(|ei|) < errLim
OR
ItCount > maxIt
End
Yes
αi = αi - ei
No
 = 1
r
(GP)
(Fixpoint)
t
s

## Slide 32: Experimental Results
[Abhijit Davare, Qi Zhu, Marco Di Natale, Claudio Pinello, Sri Kanajan and Alberto Sangiovanni-Vincentelli, “Period Optimization for Hard Real-time Distributed Automotive Systems”, DAC 2007. ]
GP optimization meets all deadlines in 1st iteration
Solution time: 24s
Maximum error reduced from 58% to 0.56% in 15 iterations
Average error reduced from 6.98% to 0.009%

## Slide 33: Problem 3: Extensibility Optimization
Extensibility metric: function of how much the execution time of tasks can be increased without violating constraints.
Utilization constraints (linear):
Latency constraints (non-linear):
Same design variables as in allocation & priority assignment. Constraints on utilization and end-to-end latency.

## Slide 34: MILP and Heuristic Hybrid Algorithm
Initial Task Allocation
(MILP approximation)
Signal Packing and Message Allocation
(weight-based heuristic)
Task and Message Priority Assignment
(iterative heuristic)
Task Re-allocation
(greedy heuristic w/ incremental changes)
Reach Stop Condition?
Yes
End
No
Initial Task and Signal Priority (heuristics)
one signal per msg
utilization constr.
latency constr. w/o extensibility factor

## Slide 35: Experimental Results
Parameter K to trade off between extensibility and latency.
Chart: Task Extensibility
| 23.803799999999889 | 23.217800000000135 | 21.447399999999814 | 21.239000000000001 | 16.911300000000001
1 bus case | 20868.4 | 16985.3 | 9136.44 | 9075.46 | 24528.1
K=0
K=0.1
K=0.2
K=0.5
manual
[Qi Zhu, Yang Yang, Eelco Scholte, Marco Di Natale and Alberto Sangiovanni-Vincentelli, “Optimizing Extensibility in Hard Real-Time Distributed Systems," RTAS 2009.]
[Qi Zhu, Yang Yang, Marco Di Natale, Eelco Scholte and Alberto Sangiovanni-Vincentelli, “Optimizing the Software Architecture for Extensibility in Hard Real-Time Distributed Systems“, IEEE TII, 2010.]

## Slide 36: End-to-End Latency
For each object in the path, add
  Period (ti)
  Worst case response time (ri)
o1
o2
o3
t1
r1
t2
r2
t3
r3
End-to-End Latency
o1
…
o2
…
o3
…
R1
R2
R3
t1
t2
t3

## Slide 37: Task Worst Case Response Time
Tasks: periodic activation and preemptive execution.
oi
Period (ti)
Response Time (ri)
Interference from higher priority tasks on the same ECU
Computation time
Interference time

## Slide 38: Task Worst Case Response Time Formulation
Task i and j need to be one the same ECU k.
Task j needs to have higher priority than i.